## Slide 1: MOD-03 Robot Kinematics & Motion Models
By Dr. Ahmad Abbadi
MOBILE ROBOTS

## Slide 2: The Problem
A company wants to build a warehouse delivery robot that must:
move between shelves
carry packages
know its position without GPS
avoid slipping when carrying heavy loads
The robot should:
drive in narrow aisles
rotate at intersections
track its position accurately

## Slide 3: The Problem
How should we mathematically describe the robot motion?
What motion is physically possible for wheeled robots?
How do we plan motion that respects these limits?
How can the robot estimate where it is?
What happens if wheels slip?

## Slide 4
A robot moving across a warehouse floor has freedom to translate and to rotate.
we need a precise mathematical relationship between
  what we control (the wheel motors) and
  what we observe (the robot's position and orientation in the warehouse).
This relationship is called the kinematic model.
Without it,
  every command we send would be a guess,
  we could not predict the robot's path, plan collision-free trajectories,
  or estimate the robot's position from sensor data.

## Slide 5
Lets divide the problem into smaller ones and think systematically.
First: what is the robot references

## Slide 6: The Frame Coordination
The Scene: A Warehouse AMR detects a shelf at [1.0,0.5] in its LIDAR frame. The robot is currently at [10.0,5.0,π/4] in the Global Map frame.
The Problem: The central server needs to update the shelf's position on the global map.
The Challenge:
  How do we communicate "where things are" across multiple moving frames of reference (Robot, Sensor, Map) without losing accuracy?
Base frame
Robot
frame
Sensor
frame
1m
{W} World Frame
Fixed to warehouse. Origin at corner. X = aisle direction. NEVER changes.
{R} Robot Body Frame
Origin at robot center. Moves with robot. Forward = +X, Left = +Y.
{S} Sensor Frame
Fixed to LIDAR mount. Static relative to {R}. Encoded in URDF.

## Slide 7: Introduction Homogeneous Transforms
Core Concept: Representing a pose as a single matrix that encodes both translation and rotation.
The Tool: The Special Euclidean Group SE(2) for planar motion.
Industry Standard: ROS TF2 (Transform Library) which automates the "Tree" of these matrices across time.

## Slide 8: Homogeneous transformation matrix - Translation Matrix
x_new = x_old + T_x
y_new = y_old + T_y
z_new = z_old + T_z

## Slide 9: Homogeneous transformation matrix - Rotation Matrix
P` = R . P

## Slide 10: Homogeneous transformation matrix
Rotation + Translation matrices
x′ = cos θ ⋅ x + (−sin θ) ⋅ y + tx
y′ = sin θ ⋅ x + cos θ ⋅ y + ty
Transformation matrix
T =
https://opentextbooks.clemson.edu/wangrobotics/chapter/forward-kinematics

## Slide 11: Homogeneous transformation matrix - Transformation Matrix
WP = WR T​ ⋅ RST​ ⋅ SP
Inversion: To go from World to Robot: RWT​=(WRT​)−1
Base frame
Robot
frame
Sensor
frame
1m
WRT =

## Slide 12: Homogeneous transformation matrix - Notes
In a 3D warehouse with ramps, can we simplify our math back to SE(2), or does the "Pitch" and "Roll" of the floor make SE(3) mandatory?
RWT = (WRT)-1 = (Computationally efficient)
we never use inv() in real-time code; we use the geometric property of the rotation matrix.

## Slide 13: The Frame Coordination
The Scene: A Warehouse AMR detects a shelf at [1.0,0.5] in its LIDAR frame. The robot is currently at [10.0,5.0,π/4] in the Global Map frame.
The Problem: The central server needs to update the shelf's position on the global map.
where things are across multiple moving frames of reference (Robot, Sensor, Map)?
You want the shelf point from LIDAR frame → Robot base frame → Global Map frame
Shelf point in sensor: pS=[1.0, 0.5]
Base frame
Robot
frame
Sensor
frame
1m
Transform R → B
we assumed a point in robot frame equals point in LIDAR frame
Homogeneous point in S
If the sensor not same as the robot frame then
go back to sensor frame

## Slide 14: Kinematic Blueprints & Constraints
The Narrow Aisle Navigation Problem
The Warehouse AMR must enter a 1.2m wide aisle, rotate 90°, and exit.
The robot is a Differential Drive platform.
The Challenge:
How to command the wheel speeds (​) to execute a "Zero-Radius Turn" without the chassis hitting the racks.

## Slide 15: Kinematic Blueprints & Constraints
https://www.roboticsbook.org/S52_diffdrive_actions.html
Move forward
Rotate
Move on curve
Why?
How to move the robot in a specific radius?

## Slide 16: Kinematic Blueprints & Constraints
The forward speed of a wheel is
Then the angular speed is
To move the robot forward
the angular speeds on the right and left wheels should be similar
https://www.roboticsbook.org/S52_diffdrive_actions.html

## Slide 17: Kinematic Blueprints & Constraints - Rotating robot
Given that the angular speeds on the wheels are
Equal but opposite forward wheel speeds
That cause the robot to rotate
Both speeds are tangent to a circle of diameter L
centered at the origin of the body-attached frame
linear velocity of the robot is zero, since and cancel one another out
The circular motion of the robot
https://www.roboticsbook.org/S52_diffdrive_actions.html

## Slide 18: Kinematic Blueprints & Constraints
The wheel velocity is the sum of linear and angular speeds
These two equations define the inverse velocity kinematics
The forward velocity kinematics are
On the robot frame the is on x axis at any time
The is tangent to the robot motion curve
Lets call it
https://www.roboticsbook.org/S52_diffdrive_actions.html

## Slide 19: Kinematic Blueprints & Constraints
The velocity of the robot in its frame
The velocity in the world frame
Combine the angular velocity with the linear one
https://www.roboticsbook.org/S52_diffdrive_actions.html
,

## Slide 20: Kinematic Blueprints & Constraints
The Narrow Aisle Navigation Problem
The Warehouse AMR must enter a 1.2m wide aisle, rotate 90°, and exit.
Calculate the exact wheel speeds required to execute a "Zero-Radius Turn" without the chassis hitting the racks.
Zero-radius turn ⇒ robot’s linear velocity is zero, so
given wheel radius r, distance between wheel centers L , and desired turn angle in T time
= 0 -
- ,

## Slide 21: Kinematic Constraints
The Warehouse AMR is on position (0,0,0) and wants to go to the delivery position on (0,2,x)
How to go there?
If a planner output
Move left 2 meters.
What is your opinion?
😏

## Slide 22: Kinematic Constraints
The Warehouse AMR is on position (0,0,0) and wants to go to the delivery position on (0,2,x)
How to go there?
If a planner output
Move left 2 meters.
Why can't the robot simply move sideways
😏

## Slide 23: Kinematic Constraints - Holonomic vs Non-Holonomic Constraints
There is a constrain
  a constraint is any condition that restricts the possible motions or configurations of a system.
A non-holonomic constraint involves velocities and cannot be integrated into a position-only equation.
For example the wheels roll without slipping, meaning the robot can only move in the direction it is currently facing.
velocity component perpendicular to the heading must be zero:
Why can't we integrate it? If we try to integrate this equation to get a position-only constraint, we fail because θ itself changes over time as the robot steers.
😏

## Slide 24: Kinematic Constraints - Holonomic vs Non-Holonomic Constraints
What if the robot should move on specific rail?
Is that limiting the velocities?
Can we reach the goal?
😏

## Slide 25: Kinematic Constraints - Holonomic vs Non-Holonomic Constraints
What if the robot should move on specific rail?
Is that limiting the velocities?
  Holonomic constrain only restrict the configuration variables (positions and angles), not their time derivatives (velocities).
  Holonomic constraints reduce the dimension of the configuration space, e.g. from 2D to 1D.
  Robot on a circular rail: A warehouse robot
  constrained to ride on a circular guide rail of radius R satisfies:
😏

## Slide 26: Kinematic Constraints - Holonomic vs Non-Holonomic Constraints
Property | Holonomic | Non-Holonomic
Depends on | Position only | Velocities
Reduces configuration space dimension | Yes | No
Restricts reachable positions | Yes — some positions are forever forbidden | No — all positions remain reachable
Restricts instantaneous velocity | Not directly | Yes — certain velocities are forbidden at each instant

## Slide 27: Kinematic Constraints - Holonomic vs Non-Holonomic Constraints
Why This Matters for Motion Planning
A planner that ignores non-holonomic constraints will
  produce trajectories the robot cannot follow.
Valid plans must ensure the robot's velocity vector is always aligned with its heading.
This is why car-like robots cannot change lanes instantaneously and why parallel parking requires a multi-step maneuver.
The non-holonomic constraint does not limit where the robot can go, but it limits how it can get there.

## Slide 28: Heavy Duty Robot
The differential driving model assumes
  perfect wheel contact with the floor,
  no wheel slipping, and
  exact motor control.
These assumptions hold well for small, lightweight warehouse robots on smooth concrete. But real vehicles behave differently.
We need a robots to move heavy pallets
To better represent steering vehicles we need different kinematics that is more accurate.
What can it Be?

## Slide 29: Kinematic Blueprints & Constraints - Bicycle Model (Car-Like Robots)
These Robot have
  a front steering axle (two wheels that turn together) and
  a rear drive axle (two fixed wheels).
Unlike the differential-drive robot,
  the driver steers by changing the angle of the front wheels
The software team needs a kinematic model for this new vehicle type. In order to generate a suitable path.
  What can we control?

## Slide 30: Kinematic Blueprints & Constraints - The Bicycle Approximation
State:
Control inputs:
  velocity
  steering angle
Rear wheels become one fixed wheel
  The rear wheel is fixed (cannot steer), so the rear axle midpoint can only move along the heading direction
https://thomasfermi.github.io/Algorithms-for-Automated-Driving/Control/BicycleModel.html
These are identical to the differential-drive equations because the rear wheel obeys the same no-lateral-slip condition

## Slide 31: Kinematic Blueprints & Constraints - The Bicycle Approximation
Two front wheels are approximated as one steering wheel.
the chassis length L,
the instantaneous center of rotation (ICR) lies on the line extending through the rear axle.
the distance from the rear axle to the ICR is:
The angular velocity of the vehicle is:
The turning radius R depends on the steering angle:
R =
https://thomasfermi.github.io/Algorithms-for-Automated-Driving/Control/BicycleModel.html

## Slide 32: Kinematic Blueprints & Constraints - The Bicycle Approximation
A practical consequence:
the forklift has a minimum turning radius
determined by the maximum steering angle of the mechanism.
This is why forklifts cannot spin in place like differential-drive robots
  they need space to turn.
Warehouse aisle widths must accommodate this minimum turning radius.
Task: The forklift has
  wheelbase L = 1.5 m and maximum steering angle φ_max = 35°.
  It approaches a 90° turn between two aisles at v = 0.8 m/s.
  What is the turning radius, and what angular velocity does the robot experience?
https://thomasfermi.github.io/Algorithms-for-Automated-Driving/Control/BicycleModel.html
R =

## Slide 33: Kinematic Blueprints & Constraints - The Bicycle Approximation
Task: The forklift has
  wheelbase L = 1.5 m and maximum steering angle φ_max = 35°.
  It approaches a 90° turn between two aisles at v = 0.8 m/s.
  What is the turning radius, and what angular velocity does the robot experience?
The forklift follows a circular arc of radius 2.14 m.
The aisle intersection must be at least this wide for the robot to make the turn
  a critical warehouse design parameter
https://thomasfermi.github.io/Algorithms-for-Automated-Driving/Control/BicycleModel.html
R =

## Slide 34: Kinematic Blueprints & Constraints - The Bicycle Approximation
Feature | Differential Drive | Bicycle / Car-Like
Spin in place | Yes () | No
Minimum turning radius | 0 (can rotate about its center) | 
Control inputs | (wheel speeds) | (speed and steering angle)
Constraint type | Non-holonomic (no lateral slip) | Non-holonomic + minimum turning radius
Typical application | Small warehouse robots, cleaning robots | Forklifts, cars, autonomous vehicles, agricultural robots
Feature | Differential Drive | Bicycle / Car-Like
Spin in place |  | No
Minimum turning radius | 0 (can rotate about its center) | 
Control inputs |  | 
Constraint type | Non-holonomic (no lateral slip) | Non-holonomic + minimum turning radius
Typical application | Small warehouse robots, cleaning robots | Forklifts, cars, autonomous vehicles, agricultural robots

## Slide 35: Kinematic Blueprints & Constraints - The Bicycle Approximation
A “bicycle model” uses a single front steering angle and single rear wheel to approximate that same car, often assuming small slip angles and moderate speeds.
A “car‑like Ackermann model” usually means you explicitly consider left and right wheel steering angles and Ackermann condition .
In practice, a bicycle model is often used as an approximation of an Ackermann‑steered car, but it is a reduced‑order model, not the full Ackermann geometry.

## Slide 36: Kinematic Blueprints & Constraints

## Slide 37: Odometry
Can we use the wheels to know the position of the robot?

## Slide 38
MOD-003 DELIVERED (Motion Model)
✅ SE(2) transforms + TF2 (S006)
✅ Diff-drive FK and IK (S009)
✅ No-slip Pfaffian constraint (S010)
✅ Ackermann bicycle model (S011)
✅ Mecanum Jacobian (S012)
✅ Maneuverability δ_M analysis (S013)
✅ Dead reckoning + covariance (S014)
✅ Slip ratio + traction control (S015)
→ PREDICT step of EKF complete
MOD-004 WILL DELIVER (Sensor Model)
📡 LIDAR range model (beam model)
📡 Gaussian measurement noise N(0, σ²)
📡 Sensor covariance matrix R_k
📡 Expected vs actual measurement h(q)
📡 Landmark detection model
📡 Log-likelihood observation
→ UPDATE step of EKF
MOD-005: EKF = PREDICT (MOD-003) + UPDATE (MOD-004)
The LIDAR correction (trigger when σ_x > 5 cm) requires a mathematical model for WHAT LIDAR measures and HOW UNCERTAIN it is.
This is exactly what MOD-004 provides. MOD-003 + MOD-004 = complete inputs for the Kalman Filter in MOD-005.

## Slide 39: ?