## Slide 1: MOD-02 Introduction to Mobile Robots
By Dr. Ahmad Abbadi
MOBILE ROBOTS

## Slide 2: Learning Objectives
Locomotion meaning and types
Distinguish holonomic from non-holonomic robots; apply morphology selection criteria
Define DOF; distinguish total DOF from controllable DOF
ROS architecture

## Slide 3: Locomotion
Focus:
Motion capability
Engineering trade-offs
Design decision making
What Locomotion means?

## Slide 4: Locomotion
Locomotion is
Physical interaction between a body and its environment, and
the interaction forces, including
  the mechanisms and actuators that generate them.
kinematics means describing
robot’s motion geometrically
The relation between the robot variables and the robot state (position, speed, heading,…)
What are the Locomotion types?

## Slide 5: Locomotion types
Wheel
Differential Drive
Ackermann Steering
Omnidirectional
Tracked
Legged
Hybrid
Locomotion types
Combine different model
Slide
Flying
Swimming

## Slide 6: Locomotion – Design Problem
Design a hospital delivery robot that must:
Navigate narrow corridors (≈ 1.2 m)
Approach beds from the side
Carry payload
Operate efficiently on battery
Question:
Which locomotion system should we choose?

## Slide 7: Locomotion – Design Problem
You solution
Can move sideways?
Can align without rotation?
Is turning space always available?
How complex it is to control the movement?
We need to make engineering decisions based on analysis

## Slide 8: Locomotion
Locomotion determines:
Mechanical complexity
Control difficulty
Degrees of freedom of motion
Maneuverability
Terrain capability
Energy consumption
robot weight and complexity
Siegwart et al., Intro to Autonomous Mobile Robots

## Slide 9: Locomotion
https://learning.edx.org/course/course-v1:ETHx+AMRx+2T2020/home
Insects can gait directly, Mammals need few hours, Humans need one year

## Slide 10: Locomotion – Legged Robot
Characteristics:
Complex mechanics
Complex control
Energy can be intensive
Advantage
Capable to move on Stairs/rubble/slopes
https://learning.edx.org/course/course-v1:ETHx+AMRx+2T2020/home

## Slide 11: Locomotion - Differential Drive Robot
Characteristics:
Simple mechanics
Can rotate in place
Cannot move sideways
Motion constrained to circular arcs
Applications:
Indoor service robots
Educational robots
Cleaning robots

## Slide 12: Locomotion - Car-Like (Ackermann Steering) Robot
Characteristics:
Front wheel steering
Stable at high speed
Efficient energy use
Large turning radius
Applications:
Autonomous cars
Outdoor delivery robots

## Slide 13: Locomotion – Tracked Robot
Characteristics:
Large contact area
High traction
Good for rough terrain
High energy consumption
Slow turning
Kinematics similar to differential drive
Difference is in physics (traction, friction).

## Slide 14: Locomotion - Omnidirectional (Mecanum / Omni Wheels) Robot
Characteristics:
Forward/backward motion
Sideways motion
Rotation simultaneously
Full planar mobility
Advantages:
Maximum maneuverability
Precise positioning
Disadvantages:
Higher energy consumption
More complex control
Lower traction efficiency
locusrobotics.com https://www.researchgate.net/figure/Omnidirectional-robot-with-three-omni-wheels_fig1_279244619

## Slide 15: Locomotion -> Motion Constraints and Holonomy
Some robots can move in any direction instantly. Others must follow constrained paths.
This difference is called holonomy.
Car
  cannot move sideways without turning first.
  It must follow a curved path.
  It is not Nonholonomic Robots
Holonomic Robots
  A robot that can move forward,
  sideways, and
  rotate simultaneously.
https://www.researchgate.net/figure/Omnidirectional-robot-with-three-omni-wheels_fig1_279244619

## Slide 16: Locomotion -> Motion Constraints and Holonomy
Holonomic robots:
✅ Maximum maneuverability ❌ Higher complexity and energy cost
Golden Rule
More freedom of motion always comes with higher cost and complexity.
can a car reach any position even though it is nonholonomic?
It can still reach any position by combining motions. Forward/ + turn + forward
Nonholonomic does NOT mean incapable. It means constrained instantaneous motion
https://www.researchgate.net/figure/Omnidirectional-robot-with-three-omni-wheels_fig1_279244619
Nonholonomic robots:
✅ Simpler and more efficient ❌ Limited motion flexibility
Notes: Is a human walking holonomic or nonholonomic?

## Slide 17: Locomotion - Engineering Comparison Summary
Type | Maneuverability | Energy | Complexity | Terrain
Differential | Medium | Low | Low | Low
Car-like | Low (tight spaces) | Low | Medium | Medium
Omni | Very high | High | High | Low
Tracked | Medium | High | Medium | Very high
No system is universally best.
Which Locomotion system is the best for hospital delivery robot?

## Slide 18: Locomotion - Engineering Comparison Summary
Which Locomotion system is the best for hospital delivery robot?
Golden rule:
Choose the simplest locomotion system
that satisfies mission requirements.
Engineering = trade-offs between:
Performance
Cost
Energy
Complexity
Terrain capability
Criterion | Importance | Score | No Go
Motion type : … |  |  | 
Performance | 1–5 |  | 
Cost | 1–5 |  | 
Energy efficiency | 1–5 |  | 
Complexity | 1–5 |  | 
Terrain capability | 1–5 |  | 
Locomotion | Score
Diff-wheel | …
Legged | …
…. | 

## Slide 19: Locomotion - Advanced Thinking Questions
What locomotion is best for Mars exploration?
NASA

## Slide 20: Locomotion - Advanced Thinking Questions
What locomotion is best for Mars exploration?
https://science.nasa.gov/mission/mars-exploration-rovers-spirit-and-opportunity/

## Slide 21: Locomotion - Advanced Thinking Questions
Why do forklifts use rear-wheel steering?
Notes: Forklifts must:
Turn in very narrow aisles
Precisely position loads
Approach shelves head-on
Carry heavy weight in the front
Rear-Wheel Steering (Forklifts)
Rotation center moves closer to the load.
Vehicle pivots around the front axle.
Much smaller turning radius.
This allows forklifts to:
✅ Turn inside narrow aisles ✅ Align precisely with shelves ✅ Rotate almost around their own footprint
This leads to a key design requirement:
Minimize turning radius while maintaining stability under load.
Rear steering disadvantages:
Less stable at high speed
Harder for human drivers to control
Oversteer risk
Not safe for highways
Forklifts operate at low speed, so this is acceptable.

## Slide 22: Locomotion - Advanced Thinking Questions
Watch Boston Dynamics Robots, and think if the leg robots is the best option for opening the door (in house, outdoor)
https://www.youtube.com/
watch?v=fUyU3lKzoio

## Slide 23: Degrees of Freedom and Controllability in Mobile Robot
What is DOF?
Distinguish between total DOF and controllable DOF

## Slide 24: Degrees of Freedom
Assuming an object on the floor.
How many motions possibility can it has?

## Slide 25: Degrees of Freedom
Assuming an object on the floor.
How many motions can it has?
A rigid body in a plane can:
  Move in x direction
  Move in y direction
  Rotate
Therefore:
  DOF in plane = 3
How many motions can you control?
Think of actuators, and how they affect the robot status (position, orientation, … )

## Slide 26: Degrees of Freedom - Differential drive robot
Differential drive robot body has:
  DOF: X,Y, Heading on plain
  2 driven wheels
Controllable DOF = 2 (forward and Angular velocities)

## Slide 27: Degrees of Freedom
Degrees of Freedom: is the number of independent parameters required to uniquely define the configuration (position and orientation) of a mechanical system.
Controlled DOF are the movements you can directly change using motors or actuators.
In simple words:
DOF = all possible independent movements
Controlled DOF = the movements you can actively command

## Slide 28: Degrees of Freedom - insights
More controllable DOF:
  Higher maneuverability − Higher complexity − Higher energy consumption
Fewer controllable DOF:
  Simpler
  Efficient − Limited motion capability

## Slide 29: Development environment
ROS architecture
Gazebo / Webpot

## Slide 30: ROS architecture – Robot SW design
Imagine we are building a warehouse mobile robot. It has:
Lidar
Camera
Obstacle avoidance algorithm
Localization algorithm
Path planner
Motor controller
Battery monitor
All running as separate software modules.”
If one module needs information from another, how should they communicate?

## Slide 31: ROS architecture – Robot SW design
What happens if we add a new module?
What if two modules want the same data?
What if the lidar updates 10 times per second?
What if one module crashes?

## Slide 32: ROS architecture – Robot SW design
Too many connections
Tight coupling
Hard to scale
No clear data flow
⚠️ Conclusion: We need structured communication

## Slide 33: ROS architecture – Communication Types
Type A: Continuous Information
Example:
Lidar continuously publishes scans.
Battery continuously reports level.
Does the obstacle avoidance module need to ask every time for lidar data?

## Slide 34: ROS architecture – Communication Types
Type B: On-Demand Request
Example:
“Reset odometry”
“Give me current robot pose”
“Compute path to goal”
Should this run continuously? Or only when requested?

## Slide 35: ROS Architecture: Nodes, Topics, Messages
docs.ros.org/
NODE (عقدة)
Independent process — one responsibility (e.g., /lidar_driver, /navigation_node)
TOPIC (موضوع)
Named async channel — /scan, /odom, /cmd_vel, /path
MESSAGE (رسالة)
Typed data struct — sensor_msgs/LaserScan, geometry_msgs/Twist
SERVICE (خدمة)
Synchronous request-response — emergency stop, mode change
TF Library
Manages coordinate frame transforms — robot body → world → map
/lidar_driver → /scan → /navigation_node → /cmd_vel → /robot

## Slide 36: ROS Architecture: Robot SW design
One node publishes.
Multiple nodes can subscribe.
Messages are sent whenever available.
Publisher does NOT know who receives.
Can multiple nodes publish to the same topic?
Can multiple nodes subscribe?
Does the publisher wait for a response?
LIDAR
/scan
Localization
Mapping
Topics are:
Asynchronous
Decoupled
Good for continuous data

## Slide 37: ROS Architecture: Topics
docs.ros.org/
Topic can receive messages from multiple nodes. And forward it to multiple node

## Slide 38: ROS Architecture: Robot SW design
The controller want to reset the odometer, values.
How to do that?
4/20/2026
38
/reset_odo
controller
Localization
?

## Slide 39: ROS Architecture: Service
docs.ros.org/
services only provide data when they are specifically called by a client

## Slide 40: ROS Architecture: Robot SW design
Client sends request.
Server processes.
Server returns response.
Communication ends.
There must be only ONE service server for a specific service. Why only one?
4/20/2026
40
/reset_odo
controller
Client
request
server
response
Localization
service
only one server because
If two servers respond, which one is correct?
Client expects exactly one answer.
Deterministic behavior required.

## Slide 41: ROS Architecture: Service
docs.ros.org/

## Slide 42: ROS Architecture
Scenario: Robot Avoiding Obstacle
Continuous sensing
Lidar publishes /scan at 10 Hz.
Obstacle Avoidance subscribes.
Is this Topic or Service?
Answer: ?
LIDAR
Obstacle Avoidance
/scan

## Slide 43: ROS Architecture
Scenario: Robot Avoiding Obstacle
Continuous sensing
Lidar publishes /scan at 10 Hz.
Obstacle Avoidance subscribes.
Is this Topic or Service?
Answer: Topic
Because
Continuous.
No request.
Many subscribers possible.
LIDAR
Obstacle Avoidance
/scan
Topic

## Slide 44: ROS Architecture
Scenario: Go to Shelf
Operator presses “Go to Shelf A”
Path Planner needs robot pose.
Should pose be continuously streamed OR requested once?
LIDAR
Localization
Obstacle Avoidance
/scan
Topic
Path planner
/pos
?

## Slide 45: ROS Architecture
Scenario: Go to Shelf
Operator presses “Go to Shelf A”
Path Planner needs robot pose.
Should pose be continuously streamed OR requested once?
If pose is continuously used → Topic.
If we just want it once → Service.
If we design:
Localization publishes /pose → Topic
Planner subscribes → continuously updated.
But if we design:
Planner calls "get_current_pose()" → Service
Then pose is returned once.
Which is better for navigation?
LIDAR
Localization
Obstacle Avoidance
/scan
Topic
Path planner
/pos
Topic

## Slide 46: ROS Architecture
LIDAR
Localization
Obstacle Avoidance
/scan
Topic
Path planner
/pos
Topic
/cmd_vel
Topic
Motor controller
Scenario: Go to Shelf

## Slide 47: ROS Architecture - Action
Actions are like services that allow you to execute long running tasks, provide regular feedback, and are cancelable.
A robot system would likely use actions for navigation.
For example an action’s “goal” tell a robot to travel to a position.
While the robot navigates to the position, it can send updates along the way (i.e. feedback),
and then a final result message
once it’s reached its destination
https://docs.ros.org/en/kilted/Tutorials/Beginner-CLI-Tools/Understanding-ROS2-Actions/Understanding-ROS2-Actions.html

## Slide 48: Development and testing
Can we develop the solution now on a real Robot?

## Slide 49: Testing
🤖 Real Hardware Testing (HIL: Hardware in the loop)
Iteration time: 10–30 min per cycle
• Deploy → crash → fix → rebuild
• Real damage: robot, environment, people
• Cannot run 100 scenarios — not scalable
🖥 Gazebo Simulation (SIL: Software in the loop)
Iteration time: 30 seconds per cycle
• Fix → restart Gazebo → retest instantly
• Zero damage risk — purely virtual
• 100+ test scenarios per hour feasible
• Waymo runs 1000× simulated miles per real mile

## Slide 50: Learning Objectives
Locomotion
Holonomic from non-holonomic robots
Define DOF; distinguish total DOF from controllable DOF
ROS architecture

## Slide 51: ?

## Slide 52: Degrees of Freedom
Why a rigid object can move sideways but cars cannot?
Does a car has 3 DOF?
We should predict the object motion capability before using it for movement.
We need a tool to answer:
How many independent motions does this system have?

## Slide 53: Degrees of Freedom - Grübler’s Formula
Let’s try Grübler’s Formula that describe the DOF for a robot
M = body freedom (3 planar / 6 spatial)
N = number of links
J = number of joints
f = joints DOF (e.g. revolute/prismatic = 1 DOF)
Conceptually:
Links add freedom.
Joints remove freedom
1 DOF
2 DOF
Notes: https://www.researchgate.net/figure/DOFs-universal-joint_fig4_281621219

## Slide 54: Degrees of Freedom - Grübler’s Formula
A differential-drive robot:
m=3 (planar).​
Links N=4: ground (1) + chassis (1) + left wheel (1) + right wheel (1).
Joints J=2: each wheel connected to chassis by a revolute joint (axle bearing).​
Joint freedoms: f1=1, f2=1 (revolute joints are 1-DOF)
??? Some thing wrong

## Slide 55: Degrees of Freedom - Grübler’s Formula
A differential-drive robot:
The connection between the ground and the platform is not representable by Grübler’s Formula.
Classical Grübler assumes:
  Rigid links
  Ideal joints
  No rolling constraints
Mobile robots violate this assumption.
So we use an extended interpretation:
Mobility = Body DOF − Nonholonomic Constraints

## Slide 56: Degrees of Freedom
How to apply the general equation:
Identify how many DOF the rigid body has
Identify touch points of the mobile robot body with the ground.
Identify where you can change the velocity on each DOF components.
  The other consider as non-holomnomic constrains.