## Slide 1
MOBILE ROBOTS
MOD-04
Sensor Modeling,
Measurement & Fusion
By Dr. Ahmad Abbadi

## Slide 2
The Big Idea: Why Do We Need This?
Every sensor on a robot tells a slightly different lie.
1. Model the Lies
Each sensor has its own type of error
We need a math model for HOW it lies
2. Measure Uncertainty
How MUCH does each sensor lie?
Express confidence as a number
"I'm 95% sure the wall is 2.0 ± 0.1m"
3. Combine Wisely
Mix all sensors, trust the reliable ones more
Result: better than any single sensor!
This is SENSOR FUSION
We learn all three using one robot: MediBot — a hospital delivery robot.

## Slide 3
Meet MediBot — Hospital Delivery Robot
The Mission
Carry medications: Pharmacy → Ward B (Floor 3)
Navigate hallways, doors, elevator
Return with blood samples from Lab
ZERO collisions — patient safety is non-negotiable
The Challenges
Polished floors → wheels slip
Glass doors → some sensors can't see glass!
People walk unpredictably
Elevator → vibration, tilt, no references
Lighting varies: bright lobby ↔ dim corridors
We will add 6 sensors, one at a time. Each fails → motivates the next.

## Slide 4
BLOCK 1
Wheel Encoders
Count wheel rotations → estimate where you are

## Slide 5
How Encoders Work — Intuition
WHEEL
→
1 revolution = N ticks (e.g., 1000)
Count ticks → distance each wheel traveled
Difference between wheels → how much robot turned
Key Equations:
Distance: Δs = (right + left) / 2
Turn: Δθ = (right − left) / wheelbase
New position:
x' = x + Δs·cos(θ),
y' = y + Δs·sin(θ)
Think of it like a pedometer for each wheel!

## Slide 6
What is Noise? — The Bell Curve
68%
← Less likely TRUE VALUE Less likely →
Every measurement has some randomness
Most readings cluster near the TRUE value (tall middle)
A few readings are way off (short edges)
We model each tick measurement as:
We describe this with TWO numbers:
μ (mean) = where the peak is
σ (std dev) = how wide the bell is
Small σ → confident sensor
Large σ → unreliable sensor
68% in | 95% in | 99.7% in

## Slide 7
The Problem: Errors Add Up!
Start
(certain)
10m
30m
80m
(LOST!)
Each ellipse = "where the robot MIGHT be"
Small ellipse = confident.
Big ellipse = lost.
With encoders alone, the ellipse ONLY GROWS.
Nothing shrinks it — because encoders only count
their own wheels. They never check the real world.

## Slide 8
FAILURE: 80m of Travel → 3m Off!
MediBot traveled 80m from pharmacy to elevator.
According to encoders: "I'm at the elevator!"
Reality: 3 meters PAST the elevator, facing the wrong wall.
Root cause: polished hospital floor → tiny slip on every turn → heading error accumulates.
The uncertainty ellipse grew and grew — nothing corrected it.
We need a sensor that measures the EXTERNAL world — walls, doors, obstacles.
The simplest option: ultrasonic sensors. Small, cheap, mount them around the robot.
→ Next: Block 2 — Ultrasonic Sensors

## Slide 9
BLOCK 2
Ultrasonic Sensors
Ping the walls with sound → measure distance

## Slide 10
How Ultrasonic Works — Intuition
SENSOR
WALL
distance = speed × time / 2
Sound travels at ~343 m/s in air
Divide by 2: sound goes THERE and BACK
BUT: speed of sound changes with temperature!
c(T) = 331.3 + 0.606·T — depends on temperature!
Cold room (15°C): 340 m/s → measures TOO SHORT
Hot room (37°C): 354 m/s → measures TOO LONG
This is a BIAS — a repeatable, predictable error
Key advantage: ultrasonic DETECTS GLASS! (sound reflects off glass, unlike some laser)

## Slide 11
Two Types of Error: Bias vs. Noise
BIAS (Systematic Error)
Same error every time — predictable
Like a clock that's always 5 minutes fast
Ultrasonic example: wrong temperature → wrong speed of sound
Fix: CALIBRATE — measure the offset, subtract it
After calibration, bias is mostly removed
NOISE (Random Error)
Different error each time — unpredictable
Like measuring your height and getting 175, 174, 176 cm...
Ultrasonic example: tiny air turbulence, timing jitter
Fix: can't remove individual noise, but can AVERAGE many readings
Or use FUSION to combine with other sensors
The Universal Sensor Equation: z = h(x) + b + v
z = what sensor says | h(x) = truth | b = bias | v = random noise

## Slide 12
FAILURE: The Open Lobby
MediBot enters the large hospital lobby (15m × 20m).
Ultrasonic max range: only 4 meters → "no reading" for distant walls.
Beam is wide (30° cone) → can't tell exact direction.
Multiple sensors firing at once → cross-talk creates phantom obstacles.
We need: MUCH longer range, MUCH finer angular resolution,
and HUNDREDS of points per scan instead of just one.
→ Next: Block 3 — LiDAR (laser scanner)

## Slide 13
BLOCK 3
LiDAR (Laser Scanner)
Spinning laser → hundreds of range points in 360°

## Slide 14
LiDAR: What Can Go Wrong? — The Beam Model
p(z) = 0.85 × p_hit + 0.05 × p_short + 0.05 × p_max + 0.05 × p_rand
p_hit (85%)
NORMAL reading
Laser hits wall, returns correct distance + small noise
This is what we WANT
Modeled as bell curve around true range
p_short (5%)
UNEXPECTEDLY CLOSE
Something between sensor and wall (person's leg, cart)
Returns shorter than expected
More likely to be close → exponential shape
p_max (5%)
MAX RANGE (missed!)
Laser hit glass (passes through!) or black surface (absorbed)
Returns maximum range value
A known FAILURE mode
p_rand (5%)
RANDOM PHANTOM
Dust, electrical noise, stray reflection
Could be ANY value
Uniform: equally likely anywhere
This model explains WHY LiDAR scans look noisy. Most beams are good (85%), but a few will always be wrong.
In ROS: this is used by AMCL (localization) to match scans to the map probabilistically.

## Slide 15
FAILURE: The Elevator Tilt
MediBot enters the elevator. It vibrates and tilts slightly.
LiDAR scan shifts — but LiDAR only sees geometry OUTSIDE the robot.
It has NO knowledge of MediBot's own rotation.
Doors open on Floor 3: heading is off by 3°.
After 20m: lateral offset = 20 × sin(3°) ≈ 1 meter → clips doorframe!
We need a sensor that FEELS motion directly.
No external reference needed — just sense your own acceleration and rotation.
→ Next: Block 4 — IMU (Accelerometer + Gyroscope)

## Slide 16
BLOCK 4
IMU (Inertial Measurement Unit)
Feel acceleration and rotation — no external reference needed

## Slide 17
IMU: The Good and the Terrible
THE GOOD
Super fast: 200 Hz (every 5 milliseconds!)
Feels every bump, tilt, turn, vibration
Works everywhere — elevator, tunnel, underwater
No external infrastructure needed
THE TERRIBLE
DRIFT: small errors accumulate over time
Gyroscope bias: heading error grows linearly (b × T)
Accelerometer: position error grows as T² (quadratic!)
After 60 seconds alone → position error = 18 METERS
IMU Error Growth Over Time
1s
0.005m
5s
0.12m
15s
0.55m
30s
2.2m
60s
18m

## Slide 18
FAILURE: 45 Seconds Without Correction
MediBot exits elevator. Crowd blocks LiDAR for 45 seconds.
IMU-only: gyro bias drifts 2.25°, position off by 1.5m.
Bigger problem: ALL corridors on Floor 3 look geometrically identical.
MediBot needs to READ the "Ward B" sign! LiDAR = geometry. IMU = motion.
Neither gives MEANING.
We need a sensor with semantic understanding — reads text, recognizes objects.
→ Next: Block 5 — Camera (RGB + Depth)

## Slide 19
BLOCK 5
Camera (RGB + Depth)
See color, texture, text — and measure depth

## Slide 20
Camera Depth: Why Far = Noisy
Stereo depth uncertainty grows as distance² (quadratic!)
At 1 meter
Depth error: ±1 cm
Very precise!
Trust this measurement a lot
Good for obstacle avoidance
At 3 meters
Depth error: ±9 cm
Getting noisy
OK for sign detection
Not great for obstacles
At 5 meters
Depth error: ±25 cm
Unreliable for navigation
Camera is "near-sighted"
This is called HETEROSCEDASTIC noise: the noise level depends on the measurement itself.
For fusion: we must tell the EKF that close readings are MORE reliable than far readings.

## Slide 21
FAILURE: Sunlight + No Rear Vision
Supply cart approaches from BEHIND at 2 m/s. Camera faces forward → can't see behind.
Afternoon sunlight through window → IR depth sensor SATURATED → depth image is noise.
Camera can't measure HOW FAST the cart moves (would need to differentiate noisy data).
We need: all-weather, rear coverage, DIRECT velocity measurement.
Radio waves don't care about light, glass, or dust!
→ Next: Block 6 — Radar (mmWave)

## Slide 22
BLOCK 6
Radar (mmWave)
Radio waves → range + angle + VELOCITY for free

## Slide 23
Radar: The Velocity Superpower
Sensor | How it gets velocity | Problem
Encoders | Differentiate position → velocity | Amplifies noise
IMU | Integrate acceleration → velocity | Accumulates bias (drift)
Radar | Doppler effect → DIRECT velocity | No drift, no noise amplification!
Radar works through glass, dust, fog, any lighting.
Each detection gives: (range, angle, velocity) — 3 measurements in 1!
Trade-off: angular resolution is 10–50× worse than LiDAR.
Two people side-by-side look like one blob to radar.

## Slide 24
6 Sensors — Each Lies Differently
Sensor | Strength | Fatal Weakness
Encoders | Fast, always available | Drift (errors only grow)
Ultrasonic | Cheap, detects GLASS | Short range, wide beam
LiDAR | Rich geometry, long range | Blind to glass, no semantics
IMU | Super fast, feels motion | Drift in seconds (T²)
Camera | Reads signs, recognizes objects | Lighting, limited FoV
Radar | All-weather, direct velocity | Low angular resolution
No single sensor is enough. But together...
Each sensor excels where another fails. The question is:
"How do we OPTIMALLY COMBINE them?" → SENSOR FUSION

## Slide 25
BLOCK 7
Sensor Fusion
Combine imperfect sensors → better than any one alone

## Slide 26
The Magic of Fusion: 1 + 1 > 2
Sensor A
σ = 5 cm
Sensor B
σ = 10 cm
→
FUSED
σ = 4.5 cm!
The fused result (4.5 cm) is better than
EITHER sensor alone (5 cm and 10 cm)!
Rule: Trust each sensor ∝ 1/uncertainty
More certain sensor gets more weight.
Less certain sensor gets less weight.
The Predict-Update Cycle
PREDICT (encoders + IMU)
"Based on motion, I think I'm HERE"
Uncertainty GROWS ↑
→
UPDATE (LiDAR / camera / radar)
"Sensor says I'm actually THERE — correct!"
Uncertainty SHRINKS ↓

## Slide 27
Block 8: When Sensors Fail — Graceful Degradation
Before accepting any measurement, ask:
"Is this reading consistent with what I expected?"
d_M < 2 → GREEN
Reading matches prediction
ACCEPT — use it in fusion
Sensor is healthy
d_M = 2–3 → YELLOW
Reading is suspicious
Accept with caution
Increase uncertainty (lower weight)
d_M > 3 → RED
Reading is almost certainly wrong
REJECT — don't use it
Flag sensor as degraded
d_M = Mahalanobis distance — measures "how surprising" a reading is, accounting for uncertainty.
Example: Camera depth fails near sunlit window → d_M spikes → auto-disabled → MediBot continues with
LiDAR + ultrasonic + radar → camera recovers in shade → d_M drops → re-enabled automatically.

## Slide 28
MediBot's Full Journey — Which Sensor Leads When?
Time | Event | Lead Sensor
0–30s | Corridor travel | LiDAR + Encoders
30s | Glass door approach | ULTRASONIC (glass!) + Camera (sign)
35–50s | Elevator ride | IMU ONLY (drift accumulates)
50s | Doors open Floor 3 | LiDAR CORRECTS → uncertainty collapses!
50–85s | Navigate to Ward B | LiDAR + Camera (reads "Ward B")
85s | Cart from behind | RADAR (detects + measures velocity)
90s | Arrive at Ward B | All sensors confirm position
Different sensors take the lead at different moments — fusion selects based on availability & reliability.

## Slide 29
Key Takeaways
1
Every sensor lies
Model HOW it lies: z = h(x) + b + v
2
Quantify uncertainty
Bell curve (Gaussian): μ = center, σ = width
3
Errors accumulate
Encoders: linear drift. IMU: quadratic (T²)!
4
No single sensor suffices
Each excels where others fail
5
Fusion makes it better
Weight by 1/uncertainty → better than any one sensor
6
Monitor health
Mahalanobis distance: reject outliers, degrade gracefully

## Slide 30
?