## Slide 1
MOBILE ROBOTS
MOD-06
Mobile Robot
Localization
By Dr. Ahmad Abbadi

## Slide 2
BLOCK A
The Localization Problem
Where am I? — The most fundamental question in mobile robotics

## Slide 3
The Problem: MediBot Wakes Up on Floor 3
3
SCENARIO:
MediBot's software crashed and rebooted.
It is somewhere on Floor 3 of the hospital.
It has a map of Floor 3, sensors are working, but it has NO IDEA where on the map it is.
How does it figure out its position?

## Slide 4
The Problem: MediBot Wakes Up on Floor 3
3
SCENARIO: MediBot's software crashed and rebooted. It is somewhere on Floor 3 of the hospital. It has a map of Floor 3, sensors are working, but it has NO IDEA where on the map it is. How does it figure out its position?
This is the LOCALIZATION problem:
Given: map m, sensor readings z₁...zₜ, controls u₁...uₜ → Find: robot pose xₜ = (x, y, θ)
The robot must figure out WHERE on the known map it is, using ONLY sensor readings and motion commands.
What the robot HAS:
A pre-built map of Floor 3
LiDAR, IMU, encoders, camera (MOD-04)
Kalman Filter math (MOD-05)
Odometry motion model (MOD-03)
What the robot DOES NOT HAVE:
GPS (indoors = no signal)
Its starting position (crashed!)
Any memory of where it was before
A human to tell it where to go

## Slide 5
Three Flavors of Localization
4
1. Position Tracking
"I roughly know where I started"
Small initial uncertainty
Track as I move
Single Gaussian works → EKF!
e.g. MediBot starts at pharmacy and tracks its way to Ward B.
2. Global Localization
"I have NO idea where I am"
Robot could be ANYWHERE on map
Need multi-modal belief
KF CANNOT handle this! → Need MCL or histogram filter
e.g. MediBot crashed, rebooted on Floor 3. Where am I?
3. Kidnapped Robot
"I THOUGHT I knew, then moved"
Was tracking correctly
Someone picked it up & moved it
Must DETECT failure + relocalize
Hardest problem!
e.g. Patient moves MediBot to
different corridor.
MOD-06 teaches algorithms for ALL three. EKF, Histogram filter, MCL.

## Slide 6
What Is a Map? What Is a Pose?
5
The Map (m)
Pre-built representation of the environment. examples
Occupancy grid: 2D grid of free/occupied cells
Feature map: set of landmarks (corners, lines)
The Pose (x)
Robot's position and orientation: x = (x, y, θ)
x, y = position in the map frame (meters)
θ = heading angle (radians)
This is what we want to ESTIMATE
It changes every time the robot moves
Localization = estimate xₜ given

## Slide 7
BLOCK B
EKF Localization
Extending the Kalman Filter to nonlinear robot models

## Slide 8
MediBot Starts at the Pharmacy (Position Tracking)
7
SCENARIO: MediBot knows it starts at the pharmacy door. It must travel to Ward B on Floor 3.
Along the way, it observes known landmarks (corridor corners detected by LiDAR).
How does it maintain an accurate position estimate as it moves?
This is POSITION TRACKING — we know roughly where we are and track from there.
MOD-05 gave us the Kalman Filter. But there's a problem:
KF Requires LINEAR Models
State transition
Observation:
A and H must be CONSTANT matrices
But robot kinematics have sin(θ) and cos(θ)!
These are NONLINEAR → KF breaks!
EKF Solution: LINEARIZE!
Replace constant A with Jacobian F(x)
Replace constant H with Jacobian H(x)
Evaluate Jacobians at current estimate
This is a LOCAL linear approximation
Works well if nonlinearity is mild
Matrix | Meaning
A | How state evolves in one step
B | How control affects state
H | What sensor measures from state
Q | Process noise (motion uncertainty)
R | Measurement noise (sensor uncertainty)

## Slide 9
Why Linear KF Breaks: The sin/cos Problem
8
This is NONLINEAR — x' depends on cos(θ), y' depends on sin(θ).
We cannot write this as x' = A·x + B·u because A would need to contain cos(θ) which changes with the state.
Solution: LINEARIZE around the current estimate x using the Jacobian.
Jacobian
F is evaluated at the CURRENT estimate θ̂ — it changes every timestep!
Key insight: The EKF is just the KF with F(x) instead of A, and H(x) instead of H. Everything else stays the same!
Diff-drive motion model (from MOD-03):

## Slide 10
The EKF Algorithm: 5 Modified Equations
9
PREDICT
1.
(nonlinear motion model)
2.
(F = Jacobian of f, evaluated at x̂ )
UPDATE
3.
(H = Jacobian of h, at x̂⁻)
4.
5.
KF → EKF changes (only 3 things!):
① Replace A·x̂ + B·u with f(x̂, u) — use the ACTUAL nonlinear model for prediction
② Replace A with F = ∂f/∂x — Jacobian of the motion model, evaluated at current estimate
③ Replace H·x̂ with h(x̂) and H with H = ∂h/∂x — Jacobian of the observation model
K, P update is IDENTICAL to KF from MOD-05.
KF:

## Slide 11
EKF-Loc: Prediction Step (Motion)
10
MediBot moves: encoders report Δs = 0.5m, Δθ = 0.1 rad
Step 1: Predict state
Use the ACTUAL nonlinear equations.
No linearization needed for the state prediction itself.
Step 2: Predict covariance
F evaluated at (x̂, θ̂, Δs, Δθ)
F = Jacobian from MOD-04 (same matrix!).
This STRETCHES the uncertainty ellipse through
the motion model. Ellipse GROWS.
Before
→ motion →
After predict
Q = process noise (from MOD-04)
Encodes: wheel slip, motor noise,
floor traction uncertainty.
After prediction: ellipse is LARGER.
Robot is less certain where it is.

## Slide 12
EKF-Loc: Observation Model (Landmarks)
11
MediBot's LiDAR detects a known corridor corner (landmark on the map).
Observation model: z = h(x) + v where z = (range, bearing) to landmark
If robot is at and landmark is at on the map:
Jacobian H = ∂h/∂x = [ −Δx/r −Δy/r 0 ]
[ Δy/r² −Δx/r² −1 ]
, r = range to landmark.
H is re-computed at each update for each landmark observation.
What this means: MediBot predicts it should see the corner at (range=3.2m, bearing=15°).
LiDAR actually measures (3.0m, 12°).
The DIFFERENCE is the innovation — used to correct the position estimate.

## Slide 13
EKF-Loc: Update Step (Correction)
12
LiDAR sees a corner. Predicted: (3.2m, 15°). Measured: (3.0m, 12°).
Innovation = z − h(x̂⁻)
= (3.0, 12°) − (3.2, 15°) = (−0.2, −3°)
"I expected to see the corner at 3.2m/15° but
saw it at 3.0m/12° — I need to correct."
K = P⁻·Hᵀ·(H·P⁻·Hᵀ + R)⁻¹
Kalman gain: balance trust between
prediction (P⁻) and sensor (R).
Same as MOD-05 — just with Jacobian H.
x̂ = x̂⁻ + K · innovation
Correct the pose: shift toward where
the landmark says we should be.
P = (I − K·H) · P⁻
Covariance SHRINKS after correction.
Ellipse gets smaller → more confident.
Before update
→ see landmark →
After update!
Each landmark observation SHRINKS the ellipse.
More landmarks = more corrections = better localization!

## Slide 14
Worked Example: MediBot — Pharmacy to Elevator
13
Step-by-step numerical example (simplified 2D, 1 landmark)
Step | x̂ (m) | ŷ (m) | θ̂ (°) | σ_x (m) | Action
Start | 0.0 | 0.0 | 0 | 0.1 | At pharmacy door (known)
Predict 1 | 2.0 | 0.0 | 0 | 0.3 | Move 2m forward (σ grows)
Update 1 | 1.95 | 0.05 | 1 | 0.12 | See corner landmark → correct!
Predict 2 | 3.95 | 0.1 | 1 | 0.25 | Move 2m more (σ grows again)
Update 2 | 3.98 | 0.08 | 0.5 | 0.09 | See 2nd landmark → even better!
Predict 3 | 5.97 | 0.12 | 0.5 | 0.22 | Move 2m (approaching elevator)
Update 3 | 6.01 | 0.03 | 0.2 | 0.07 | See elevator door landmark
Pattern: σ grows at each predict, shrinks at each update. More landmarks = tighter estimate.
After 3 predict-update cycles: error is only 1 cm (started at 10 cm). EKF works beautifully for position tracking!

## Slide 15
EKF Localization: Summary & Limitations
14
✅ EKF Strengths
Computationally efficient: O(n²) per landmark
Well-understood, easy to implement
Works great for position tracking
Standard in ROS (robot_localization)
Handles multiple sensor types naturally
❌ EKF Limitations
Maintains SINGLE Gaussian → can't handle multiple hypotheses ("am I in room A or B?")
Linearization fails for LARGE nonlinearities
Can DIVERGE if initial estimate is too far off
Cannot recover from wrong initialization
SCENARIO: MediBot crashed and rebooted.
It could be in corridor A, corridor B, or near the elevator — three possible locations.
The EKF maintains ONE Gaussian bell curve — it can only represent ONE hypothesis.
How do we handle MULTIPLE possibilities?
→ We need algorithms that can represent MULTI-MODAL beliefs. Next: Histogram Filter and MCL.

## Slide 16
Example
Setup: Robot in a Corridor with 3 Landmarks
16
Corridor is 10m long. Robot starts at x=1m. Three landmarks at x=3, 6, 9m.
0
1
2
3
4
5
6
7
8
9
10
L₁
L₂
L₃
Parameters:
Parameter | Value | Meaning
Initial state x̂₀ | 1.0 m | Robot starts at position 1m
Initial uncertainty σ₀ | 0.5 m | We know start ± 0.5m
Motion noise Q | 0.1 m² | Each move adds 0.1m² variance
Sensor noise R | 0.04 m² | LiDAR range noise σ = 0.2m

## Slide 17
Example
Cycle 1: Predict (Move 2m) → Update (See L₁)
17
PREDICT: Move right 2m
x̂⁻ = x̂ + u = 1.0 + 2.0 = 3.0 m
P⁻ = P + Q = 0.25 + 0.1 = 0.35 m²
σ⁻ = √0.35 = 0.59 m
Uncertainty GREW: 0.5m → 0.59m
UPDATE: See landmark L₁ at 3m
Expected range: h(x̂⁻) = |3 − 3.0| = 0.0 m
Let measured range: z = 0.15 m (noisy)
Innovation: 0.15 − 0.0 = 0.15 m
K = P⁻/(P⁻+R) = 0.35/0.39 = 0.90
x̂ = 3.0 + 0.90×0.15 = 3.135 m
P = (1−0.90)×0.35 = 0.035 m² → σ = 0.19 m
Result: σ dropped from 0.59m → 0.19m! Seeing ONE landmark cut uncertainty by 3×.
K = 0.90 means: trust the sensor 90%, trust prediction 10% (because sensor R=0.04 << P⁻=0.35).
O
OPERATE: If no landmarks visible, σ keeps growing. EKF depends on regular landmark observations for correction.

## Slide 18
Example
Cycles 2–3: Convergence Over Time
18
Step | x̂ (m) | σ (m) | K | What happened
Start | 1.00 | 0.50 | — | Initial belief
Predict 1 | 3.00 | 0.59 | — | Moved 2m → σ grew
Update 1 (L₁) | 3.14 | 0.19 | 0.90 | Saw L₁ → σ collapsed!
Predict 2 | 5.14 | 0.29 | — | Moved 2m → σ grew
Update 2 (L₂) | 5.98 | 0.15 | 0.68 | Saw L₂ → σ shrank
Predict 3 | 7.98 | 0.25 | — | Moved 2m → σ grew
Update 3 (L₃) | 8.96 | 0.13 | 0.61 | Saw L₃ → best yet!
Key observations:
1. K decreases over time (0.90 → 0.68 → 0.61) because P is getting smaller → trusting prediction more
2. σ after each update gets smaller: 0.19 → 0.15 → 0.13 → converging!
3. The predict-update pattern is clear: predict GROWS uncertainty, update SHRINKS it

## Slide 19
BLOCK D
Markov Localization
& Histogram Filter
Handling global localization with a grid-based approach

## Slide 20
MediBot Rebooted — Where on Floor 3?
20
SCENARIO: MediBot crashed and has NO idea where it is on Floor 3. It could be in ANY corridor. The EKF needs a good initial guess — but we don't have one! We need an algorithm that can represent 'I might be ANYWHERE' and narrow down as evidence comes in.
Solution: Discretize the space into a grid. Assign a probability to EACH cell.
Uniform distribution: each cell has equal probability (1/20 = 5%)
"I might be anywhere" — this is something EKF CANNOT represent!

## Slide 21
Histogram Filter: The Algorithm
21
PREDICT: Shift + Blur
For each cell xₖ: bel⁻(xₖ) = Σᵢ p(xₖ|xᵢ, u) × bel(xᵢ)
"Shift probabilities in the direction of motion.
Blur because motion is noisy."
UPDATE: Multiply by Likelihood
For each cell xₖ: bel(xₖ) = η × p(z|xₖ) × bel⁻(xₖ)
"Multiply each cell's probability by how
well the sensor reading matches that cell.
Then normalize so probabilities sum to 1."
This is the EXACT Bayes filter from MOD-05 — just computed on a discrete grid instead of continuous!
Classic Example: The Door Sensor
Floor 3 has doors at cells 3, 7, 14. Sensor reports: "I see a door."
After seeing "door": cells with doors get HIGH probability, others get LOW. Three peaks = multi-modal!

## Slide 22
Histogram: Advantages & Limitations
22
✅ Advantages
Handles MULTI-MODAL beliefs (multiple peaks)
Can represent 'I might be anywhere' (global loc)
No linearization needed — exact Bayes filter
Works for any distribution shape
Simple to understand and implement
❌ Limitations
EXPONENTIAL in dimensions!
2D: 1000×1000 grid = 1 million cells
3D (x,y,θ): 1000×1000×360 = 360 million!
Fixed resolution: can't zoom in on good areas
Memory-intensive for large environments
Impractical for most real robots
SCENARIO: Floor 3 of the hospital is 50m × 30m. With 10cm resolution and 1° angle bins: 500 × 300 × 360 = 54 MILLION cells. Each needs a probability value. Too many! We need a smarter representation that puts more detail where it matters and less where it doesn't.
→ Solution: represent the belief with SAMPLES (particles) instead of a grid. Next: MCL!

## Slide 23
BLOCK E
Particle Filters &
Monte Carlo Localization
Sample-based localization that handles everything

## Slide 24
MediBot Rebooted — MCL to the Rescue
24
SCENARIO: MediBot has NO idea where it is.
We can't use EKF (needs good initial guess).
Histogram is too expensive (54 million cells).
Instead: scatter 1000 random 'guesses' (particles) across the map.
As MediBot moves and senses, the good guesses survive and bad guesses die.
Each particle = one possible robot pose (x, y, θ)
1000 particles scattered randomly → "I might be ANYWHERE"
Over time, particles will CLUSTER around the true position as evidence accumulates.

## Slide 25
The MCL Algorithm: 3 Steps
25
1. PREDICT (Move)
For each particle:
Sample new pose from p(x'|x, u)
Apply the motion model + ADD random noise
Each particle moves slightly differently (because noise is random per particle)
2. WEIGHT (Sense)
For each particle:
w = p(z | x_particle)
"How well does the sensor reading match this particle's position?“
Good match → HIGH weight
Bad match → LOW weight
Use MOD-04 sensor model as p(z|x)
3. RESAMPLE
Draw N new particles from the old ones, WITH REPLACEMENT, proportional to weights.
High-weight particles get COPIED
Low-weight particles DIE
Result: particles cluster near
the true position!
Repeat: Move → Weight → Resample → Move → Weight → Resample → ... Particles converge!

## Slide 26
After 1
observation
MCL Visual: Particles Converging Over Time
26
Start:
Scattered
After 3
observations
After 10
observations
Scattered → Clustering → Concentrated → Converged!
Each resample step KILLS bad particles and CLONES good ones. Natural selection for robot poses!
https://robots.stanford.edu/videos.html

## Slide 27
MCL: The Math Behind Each Step
27
Step 1 — Predict:
Sample from the motion model.
Each particle gets a different random noise realization.
Step 2 — Weight:
Evaluate the sensor model at each particle's pose.
High weight = sensor reading matches well at this particle's position.
Step 3 — Resample: Draw N particles with probability ∝ w_particle
Multinomial resampling: each old particle is picked with probability proportional to its weight.
Particle with weight 0.1 gets picked ~10% of the time. Weight 0.001 → almost never picked → dies.
Total computational cost per step: O(N × K) where N = particles, K = sensor beams. Typically N = 500–5000.

## Slide 28
Kidnapped Robot Recovery
28
SCENARIO: MediBot was tracking correctly in corridor A.
A patient accidentally pushes it to corridor C.
MediBot's particles are all in corridor A — WRONG.
How does it recover?
The Problem: Particle Deprivation
All particles are in corridor A
Sensor readings don't match corridor A
All weights become very small
After resampling: same bad particles copied
Robot is STUCK with wrong belief

## Slide 29
Kidnapped Robot Recovery
28
SCENARIO: MediBot was tracking correctly in corridor A.
A patient accidentally pushes it to corridor C.
MediBot's particles are all in corridor A — WRONG.
How does it recover?
The Problem: Particle Deprivation
All particles are in corridor A
Sensor readings don't match corridor A
All weights become very small
After resampling: same bad particles copied
Robot is STUCK with wrong belief
The Fix: Random Injection
After each resample, inject a small % of RANDOM particles across the map
These random particles "explore" new areas
If robot IS in corridor C, random particles there will get HIGH weights and multiply!
This is what makes MCL robust to kidnapping
AMCL (Adaptive MCL) in ROS does this automatically:
it monitors the average weight and adds random particles when it detects the robot is lost.

## Slide 30
MCL: Strengths & Limitations
29
✅ MCL Strengths
Handles multi-modal beliefs (global loc!)
Handles kidnapped robot (with random injection)
Non-parametric: any distribution shape
Computationally scalable (adjust N particles)
Works with any sensor model from MOD-04
Standard in ROS: AMCL package
❌ MCL Limitations
More particles = better but slower
Particle deprivation in high-dimensional spaces
Resampling can lose diversity (particle starvation)
Not as smooth as EKF for position tracking
Needs a good sensor model to weight correctly
Not suitable for very high-speed applications
O
OPERATE: In practice: use AMCL for global localization, switch to EKF for smooth tracking once converged. Many systems run BOTH.

## Slide 31
BLOCK F
Algorithm Comparison
Which algorithm for which problem?

## Slide 32
EKF vs. Histogram vs. MCL — Head to Head
31
Property | EKF | Histogram | MCL
Belief type | Single Gaussian | Discrete grid | Particle set
Multi-modal? | NO | YES | YES
Global localization? | NO | YES | YES
Kidnapped recovery? | NO | YES (slow) | YES (fast)
Computational cost | O(n²) — fast! | O(cells) — exponential in dim | O(N×K) — tunable
Smoothness | Very smooth | Quantized (grid) | Noisy (sampling)
Implementation | Medium | Easy | Medium
ROS package | robot_localization | — | AMCL (Nav2)

## Slide 33
Decision Flowchart: Which Algorithm to Use?
32
Localization needed
Do you know the starting position?
YES
Use EKF
(position tracking)
NO
Real-time needed?
Use MCL / AMCL
(global + kidnapped)
Best practice: Use BOTH!
AMCL for initial global localization.
Once converged → switch to EKF for smooth tracking.

## Slide 34
BLOCK G
AMCL in ROS 2 / Nav2
From theory to practice: running localization on a real robot

## Slide 35
What Is AMCL? (Adaptive Monte Carlo Localization)
34
AMCL = the standard localization algorithm in ROS 2 Nav2 stack.
What AMCL adds to basic MCL:
ADAPTIVE particle count: more particles when
uncertain, fewer when confident → saves CPU
KLD-sampling: auto-tunes particle count
Random particle injection: recovers from kidnap
Laser scan matching: uses likelihood field model
Runs as a Nav2 lifecycle node
Inputs and outputs:
INPUTS:
/scan (sensor_msgs/LaserScan) — LiDAR data
/map (nav_msgs/OccupancyGrid) — pre-built map
/tf (odom → base_link) — odometry transform
OUTPUTS:
/tf (map → odom) — global pose correction
/amcl_pose — estimated pose with covariance
KLD sampling, Kullback-Leibler Divergence sampling, is a method used in particle filters to optimize the number of particles needed for effective state estimation in dynamic systems. Based on the concentration of the probability density function.

## Slide 36
Key Takeaways
37
1
EKF = position tracking
Fast, smooth, but needs good initial guess. One Gaussian.
2
Histogram = exact Bayes
Multi-modal but exponential in dimensions. Impractical for 3D.
3
MCL = the workhorse
Handles global loc + kidnap. Tunable particles. Used in ROS.
4
Linearization = key EKF trick
Replace A with Jacobian F(x). Same idea from MOD-04.
5
Use both in practice
AMCL for initial localization, EKF for smooth tracking.
6
Theory → ROS → Robot
MOD-04 noise → MOD-05 Bayes → MOD-06 algorithms → AMCL.

## Slide 37
Bridge to MOD-07: Perception
38
What MOD-06 assumed → What MOD-07 will provide:
MOD-06 assumed: "We can detect landmarks" — but HOW? That's perception (MOD-07).
MOD-06 assumed: "We know which landmark is which" — but HOW? That's data association (MOD-07/08).
MOD-06 assumed: "We have a map" — but HOW do we build one? That's SLAM (MOD-08).
MOD-07 (Perception) fills the gap: raw sensor data → detected objects → identified landmarks → fed to localization.
The autonomy pipeline so far:
Sensors
(MOD-04)
→
Probability
(MOD-05)
→
Localization
(MOD-06)
→
Perception
(MOD-07)
→
Planning
(MOD-09)
SLAM
(MOD-08)

## Slide 38
References
39
1. Thrun, Burgard & Fox (2005). Probabilistic Robotics. MIT Press. Ch. 7–8.
2. Dellaert, F. et al. (1999). Monte Carlo Localization for Mobile Robots. ICRA.
3. Fox, D. et al. (2001). KLD-Sampling: Adaptive Particle Filters. NIPS.
4. Thrun, S. (2002). Particle Filters in Robotics. UAI.
5. robot_localization ROS package: github.com/cra-ros-pkg/robot_localization
6. Nav2 AMCL documentation: docs.nav2.org/configuration/packages/configuring-amcl.html
7. Siegwart, Nourbakhsh & Scaramuzza (2011). Intro to Autonomous Mobile Robots. Ch. 5.
Next: MOD-07 — Robot Perception (perception pipeline, visual odometry, object detection)

## Slide 39
?

## Slide 40
Key AMCL Parameters You Must Configure
35
Parameter | Default | Meaning | Tune when...
min_particles | 500 | Minimum number of particles | Robot is always confident → lower
max_particles | 2000 | Maximum when uncertain | Large map → increase
laser_model_type | likelihood_field | How scan matches map | Almost always use likelihood_field
odom_model_type | diff-corrected | Odometry noise model | Match your robot type
recovery_alpha_slow | 0.001 | Slow average weight filter | Higher → faster kidnap detection
recovery_alpha_fast | 0.1 | Fast average weight filter | Higher → more random particles
update_min_d | 0.25 m | Min move before update | Lower → more updates, more CPU
update_min_a | 0.2 rad | Min rotation before update | Lower → updates on small turns
These parameters directly connect to MOD-04 (sensor noise) and MOD-05 (Bayes filter). Theory → practice!

## Slide 41
AMCL: What You Implement in the Lab
36
C
CONCEIVE: Understand: AMCL = MCL + adaptive particles + random injection for kidnap recovery.
D
DESIGN: Choose parameters: min/max particles, laser model, odom model based on YOUR robot's sensors (MOD-04 noise values).
I
IMPLEMENT: Configure AMCL YAML file, set up TF tree (map→odom→base_link), launch with Nav2.
O
OPERATE: Test: place robot in known position → verify AMCL converges. Then try 'kidnap' test → verify recovery.
Launch commands:
# Launch AMCL with your map:
ros2 launch nav2_bringup localization_launch.py map:=/path/to/map.yaml
# Verify topics:
ros2 topic echo /amcl_pose # Check pose estimate
ros2 run tf2_tools view_frames # Verify TF tree is complete