## Slide 1
MOBILE ROBOTS
MOD-08
Mapping & SLAM
By Dr. Ahmad Abbadi

## Slide 2
BLOCK A
Why SLAM?
The chicken-and-egg problem of robotics

## Slide 3
PBL: MediBot on a NEW Floor — No Map Exists
3
PBL SCENARIO: Hospital opens Floor 4.
No map exists.
Localization (MOD-06) needs a map.
Planning (MOD-09) needs a map.
To build a map, the robot needs to know where it IS. Neither is known! This is SLAM: solve BOTH simultaneously.
The Chicken-and-Egg:
Localization needs a MAP
Mapping needs a POSE
Neither is known!
SLAM: solve BOTH at once
SLAM = Simultaneous Localization And Mapping
Estimate robot pose AND map together
No prior map — build as you go
Most important problem in mobile robotics
Practical solutions since ~2005
SLAM: estimate
Joint posterior over trajectory x AND map m, given sensors z and controls u.
Much harder than localization alone
map is ALSO unknown,
uncertainties are correlated.

## Slide 4
SLAM Taxonomy: What We Cover
4
Algorithm | Map Type | Approach
Occupancy Grid | Grid (free/occ) | Log-odds, known pose
EKF-SLAM | Feature landmarks | Gaussian, O(n^2)
FastSLAM | Feature or grid | Rao-Blackwell particles
Graph-SLAM | Pose graph | Least-squares optimize
Visual SLAM | Keyframes+features | Feature/direct methods

## Slide 5
BLOCK B
Occupancy Grid Map building
Building a grid map when pose IS known

## Slide 6
Log-odds: Efficient Belief Update for Grid Cells
6
Log-odds:
Update:
Convert probability to log-odds -> updates become ADDITION (efficient!).
= prior (usually = 50%). Each reading adds/subtracts evidence. No overflow.
Sensor says OCCUPIED:
Add positive evidence:
(strong evidence)
After many hits: l -> large positive -> p~1
Cell converges to OCCUPIED
Sensor says FREE (ray passes):
Add negative evidence:
(moderate evidence)
After many passes:
Cell converges to FREE
Convert back: This is the map Nav2 uses as static costmap layer!

## Slide 7
Inverse Sensor Model: Raytrace to Update Cells
7
SCENARIO: For each LiDAR beam: mark cells along the beam as FREE, mark the endpoint as OCCUPIED. Bresenham line algorithm efficiently finds all grid cells the ray passes through.
For each beam: raytrace robot->endpoint -> mark FREE along ray -> mark OCCUPIED at end
This is EXACTLY how Nav2 obstacle costmap layer works. Parameter: raytrace_range.
This works IF pose is known:
Each beam updates correct cells
Map converges to accurate occupancy
Standard technique, very reliable
Used by gmapping, slam_toolbox
Fails IF pose is WRONG:
Beams update WRONG cells
Map becomes corrupted, blurred
Walls appear thick/doubled
-> This is why we need SLAM!
Occupancy mapping = the MAPPING half of SLAM. Next: how robots REPRESENT these maps.

## Slide 8
BLOCK C
Map Representations
Six ways to store and reason about the world

## Slide 9
Overview: Six Map Types
9
The choice of map affects: memory, accuracy, planning capability, and which SLAM algorithm to use.
Occupancy Grid
Feature/Landmark
Topological Graph
Point Cloud 3D
Octree (OctoMap)
Semantic Map
Real systems combine multiple types. Each makes different trade-offs.

## Slide 10
Metric: Occupancy Grid & Feature Map
10
Occupancy Grid (most common)
2D grid: free/occupied/unknown per cell
Resolution: 5-10 cm typical
50m x 30m at 5cm = 600K cells
Pro: exact geometry, Nav2 compatible
Pro: easy update from LiDAR (log-odds)
Con: fixed resolution, 2D only
Format: nav_msgs/OccupancyGrid
Feature / Landmark Map
Sparse landmarks: (x, y, type)
Corners, lines, distinctive points
Pro: very compact (100 vs 600K cells)
Pro: naturally used by EKF-SLAM
Con: no free-space info for planning
Con: needs distinctive features
Used by: EKF-SLAM, visual SLAM
Occupancy = 'Is this cell free?’
Feature = 'Where are landmarks?’
Often used together.

## Slide 11
Topological Maps: Graphs of Places
11
Represent environment as a GRAPH:
nodes = places,
edges = connections between them.
Advantages:
Very compact, natural for high-level planning
'Go to pharmacy then elevator'
Scales to entire buildings, multi-floor
Limitations:
No metric detail (exact positions)
Can't do fine obstacle avoidance
Pharmacy
Corridor A
Elevator
Corridor B
Ward B
Lab

## Slide 12
3D Maps: Point Clouds, Voxels & Octrees
12
Point Cloud Map
Raw 3D points from LiDAR/depth
Very detailed, exact geometry
Millions of points = huge memory
No free/occupied distinction
sensor_msgs/PointCloud2
Octree (OctoMap)
3D occupancy grid, ADAPTIVE resolution
Fine near surfaces, coarse in open space
Huge memory savings vs uniform voxels
Stores free/occupied/unknown
Standard: octomap ROS package
Elevation Map (2.5D)
One height per (x,y) cell
Simpler than full 3D
Good for outdoor terrain
Can't represent overhangs/tunnels
elevation_mapping ROS package
Indoor flat floor: 2D grid.
Outdoor terrain: 2.5D elevation.
Complex 3D: octree.
Dense reconstruction: point cloud.

## Slide 13
Semantic Maps: Adding Meaning to Geometry
13
Standard Occupancy Grid:
Cell = free (0) or occupied (100)
No difference: wall vs door vs person
Everything is just 'obstacle'
Can't make intelligent decisions
Semantic Map:
Cell = free + label (floor, corridor, room)
Objects = type + position (door, chair)
'Go to the kitchen' (not just coordinates)
'Door may open/close' (dynamic behavior)
Semantic maps combine perception + mapping.
Active research area.

## Slide 14
Map Representation Comparison
14
Type | Memory | Planning | SLAM Algorithm | Best for
Occupancy Grid | Medium | Excellent | FastSLAM, Graph | Indoor 2D nav
Feature/Landmark | Low | Not directly | EKF-SLAM | Small environments
Topological | Very Low | High-level | Place recognition | Multi-floor
Point Cloud | Very High | Needs processing | LiDAR SLAM | 3D reconstruction
Octree | Adaptive | 3D planning | 3D SLAM | UAVs, manipulation
Semantic | Medium+ | Intelligent | Research frontier | Service robots
Real systems use MULTIPLE representations simultaneously.

## Slide 15
BLOCK D
SLAM Problem Formulation
The mathematical structure

## Slide 16
SLAM as a Joint Estimation Problem
16
Full SLAM:
Online SLAM:
Full = entire trajectory + map (graph-SLAM).
Online = current pose + map (EKF-SLAM, FastSLAM).
Why harder than localization:
Map m is UNKNOWN
Landmark positions are uncertain
Correlations: observing L1 informs L2
Through shared robot pose uncertainty
The key insight: CORRELATIONS
Observe A and B from same pose -> correlated
Correcting A also corrects B!
Full covariance matrix captures this
Off-diagonal elements are NOT zero

## Slide 17
Three SLAM Approaches: How They Differ
17
EKF-SLAM (Block F)
One big Gaussian: robot + all landmarks
Maintains full correlations
O(n^2) per step — quadratic!
Best: small maps (<100 landmarks)
Online: processes data as it arrives
FastSLAM (Block G)
Particles for pose + EKF per landmark
No full correlation matrix needed
O(M*N*log N) — much faster
Best: medium maps, grid maps
Online: particle filter updates
Graph-SLAM (Block H)
Pose graph + constraint optimization
Can fix OLD errors retroactively
Batch or incremental solvers
Best: large-scale, city-scale
Modern standard: used everywhere
Each exploits the SLAM structure differently.
Let's dive into each algorithm.

## Slide 18
BLOCK E
Data Association
Which landmark am I seeing?

## Slide 19
PBL: Two Similar Corners — Which Is Which?
19
PBL SCENARIO: MediBot detects a corridor corner.
Map has 5 known corners. Which one?
Wrong association -> EKF corrects wrong landmark -> map corrupts, localization diverges.
Data association is CRITICAL.
Nearest Neighbor
Match to CLOSEST landmark
Euclidean distance
Simple, fast
Fails with dense landmarks
Mahalanobis Gating
Accounts for UNCERTAINTY shape
Reject if (outlier)
Then pick nearest within gate
Max. Likelihood (ML)
Compute
Pick landmark with highest p
Most principled, more expensive
Joint compatibility for all matches
Wrong data association = #1 cause of SLAM failure.
Always use Mahalanobis gating at minimum.

## Slide 20
New Landmark vs. Known Landmark
20
Decision rule:
: MATCH known
: NEW landmark
-> initialize new landmark in state
Threshold choice is critical
When association is WRONG:
Match wrong -> EKF pulls to wrong position
Create false new -> phantom landmarks grow
Merge two real -> lose information
'SLAM is only as good as its data association'

## Slide 21
BLOCK F
EKF-SLAM
One big Gaussian over robot + all landmarks

## Slide 22
Augmented State Vector
22
State:
Size: (3+2n) x 1 where n = number of landmarks
Robot pose (3 DOF) + all landmark positions (2 DOF each) in ONE state vector.
50 landmarks: state = 103 elements. Covariance: 103x103 = 10,609 elements!
Key: off-diagonal blocks encode CORRELATIONS. Observing one landmark improves the ENTIRE map.
Covariance structure:
P_rr: robot uncertainty (3x3)
P_rl: robot-landmark cross-corr
P_ll: landmark-landmark cross-corr
All are maintained and updated
The 'magic':
Observe landmark j -> K corrects ALL
Cross-correlations propagate correction
Landmarks far from j also improve!
This is why EKF-SLAM works

## Slide 23
EKF-SLAM: Predict + Update
23
Predict:
Only robot part changes (landmarks don't move). F = block diagonal .
Update:
H = Jacobian of observation (sparse: only robot + matched landmark columns non-zero).
Innovation:
Predicted range/bearing to landmark j vs actual measurement. K has (3+2n) rows -> corrects EVERYTHING.
Key: K has (3+2n) rows. Observing landmark j corrects robot AND all landmarks through correlations.

## Slide 24
EKF-SLAM: Worked Example (2 Landmarks)
24
Step | State [x,y,L1x,L1y,L2x,L2y] | sigma_robot | Action
Start | [0, 0, -, -, -, -] | 0.1m | Known start
See L1 | [0, 0, 3.0, 0.5, -, -] | 0.1m | Initialize L1
Move 1m | [1.0, 0, 3.0, 0.5, -, -] | 0.25m | Uncertainty grew
See L1 again | [0.95, 0.02, 2.98, 0.49, -, -] | 0.12m | L1 corrects robot!
See L2 | [0.95, 0.02, 2.98, 0.49, 5.1, -0.3] | 0.12m | Initialize L2
See L1+L2 | [0.97, 0.01, 2.99, 0.50, 5.08, -0.28] | 0.08m | Both correct map!
Seeing L1 also improved L2 through cross-correlations. This is the EKF-SLAM magic.

## Slide 25
EKF-SLAM: Cost & Limitations
25
Strengths:
Maintains full correlations
Converges over time
Well-understood math
Simple implementation
Good for small-medium maps
Limitations:
O(n^2) per update — quadratic!
100 landmarks -> 10K ops/step
1000 landmarks -> 1M ops -> too slow
Linearization errors accumulate
Single Gaussian -> no ambiguity
For >100 landmarks: too expensive. FastSLAM solves this with particles.

## Slide 26
BLOCK G
FastSLAM
Particles for pose + mini-EKFs for landmarks

## Slide 27
Rao-Blackwellization: The Key Idea
27
IF we know the path, landmarks become INDEPENDENT. No cross-correlations needed!
Rao-Blackwellization:
PARTICLES for robot path
Separate mini-EKFs per landmark PER PARTICLE
Each particle: 1 pose + N small 2x2 EKFs
No huge covariance matrix!
Why faster:
EKF-SLAM: (3+2n)x(3+2n) matrix -> O(n^2)
FastSLAM: M particles x N independent 2x2 EKFs
O(M*N) ~ O(M*N*log N) with trees
1000 landmarks: 50K vs 1M operations!

## Slide 28
FastSLAM: 4 Steps per Particle
28
1. SAMPLE Pose
For each particle:
x' ~ p(x'|x, u)
Sample motion model
(like MCL, MOD-06)
2. WEIGHT
How well does observation match THIS particle’s pose and landmark?
3. UPDATE Map
For matched landmark:
mini-EKF update (2x2)
For new landmark:
initialize new 2x2 EKF
4. RESAMPLE
Draw N new particles by weight (like MCL)
High-weight: COPIED with their entire map!
Low-weight: DIE
Each particle carries its OWN map. After resampling, best maps survive. Natural selection!

## Slide 29
FastSLAM: Worked Example
29
Step | Particle 1 | Particle 2 | Particle 3
Pose after move | (1.02, 0.01) | (0.98, -0.03) | (1.05, 0.04)
See L1: weight | w=0.65 (good) | w=0.25 | w=0.10 (bad)
L1 EKF update | L1=(3.01, 0.48) | L1=(2.95, 0.52) | L1=(3.08, 0.55)
After resample | Survived (x2) | Survived (x1) | DIED
Particle 1 had best pose -> highest weight -> cloned. Its (good) map survives. Particle 3 dies with its bad map.

## Slide 30
FastSLAM: Strengths & Limitations
30
Strengths:
O(M*N*log N) — much faster than EKF
Handles nonlinear motion naturally
Multi-modal data association possible
Works with occupancy grids (FastSLAM 2.0)
Each particle can have different associations
Limitations:
Particle deprivation (same as MCL MOD-06)
Resampling destroys map diversity
Doesn't capture full landmark correlations
Needs many particles for good results
Map copying during resample is expensive

## Slide 31
BLOCK H
Graph-Based SLAM
Pose graphs + optimization — the modern standard

## Slide 32
From Filtering to Optimization
32
Filtering (EKF/FastSLAM):
Process one measurement at a time
Cannot fix old estimates
Linearization errors accumulate
Good for: small maps, real-time
Optimization (Graph-SLAM):
Collect constraints, optimize all at once
CAN fix old errors retroactively
Batch or incremental solvers
Good for: large maps, highest accuracy
Graph-SLAM dominates modern SLAM.
Used by: slam_toolbox, Cartographer, ORB-SLAM, LIO-SAM.

## Slide 33
Pose Graph: Nodes, Edges & Loop Closures
33
Nodes = robot poses.
Edges = constraints (odometry, loop closure, landmark observations).
Edges (constraints):
Odometry:
Loop closure: (same place!)
Landmark: saw landmark at position p
Loop closure is KEY:
Detect: 'I've been HERE before!'
Add constraint:
Optimize -> distributes error across loop
Entire map corrects retroactively!
Without loop closure: maps drift.
With loop closure: maps become globally consistent.

## Slide 34
Graph-SLAM: The Math — Least Squares Optimization
34
Minimize:
For each edge (i,j): error = predicted - actual. 𝜴 = information matrix (inverse covariance).
Find poses x that minimize TOTAL weighted error across ALL edges.
Gauss-Newton: then x <- x + dx
H = Jacobian of all errors. Sparse system -> efficient solvers (g2o, GTSAM, Ceres).
You don't implement from scratch! Libraries:
g2o: general graph optimization (ORB-SLAM, many ROS tools)
GTSAM: factor graph library by Georgia Tech
Ceres: Google's nonlinear solver (Cartographer)

## Slide 35
Graph-SLAM: Architecture Overview
35
Modern graph-SLAM systems have a front-end and a back-end:
Front-End (sensor processing):
Scan matching (ICP, NDT) for LiDAR
Feature matching (ORB) for camera
Produces: relative pose constraints
Detects loop closures (BoW, scan match)
Runs in real-time
Back-End (optimization):
Receives constraints from front-end
Builds pose graph incrementally
Runs optimization (Gauss-Newton/LM)
Outputs: optimized trajectory + map
Can run in background thread
Front-end: WHAT constraints exist.
Back-end: BEST poses given constraints.
Clean separation!

## Slide 36
BLOCK I
Loop Closure Detection
Recognizing places you've visited before

## Slide 37
Three Approaches to Loop Closure
37
Scan Matching (LiDAR)
Compare current scan to history
ICP: align two point clouds
Works in structured environments
Fails in featureless areas
Bag of Words (Camera)
ORB features -> visual words
Compare bags: similar = same place
DBoW2 library (ORB-SLAM)
Fast: O(1) lookup with inverted index
Deep Learning Place Recog.
Image -> descriptor vector (NetVLAD)
Cosine similarity for matching
More robust to viewpoint change
Requires GPU
FALSE loop closures are CATASTROPHIC — they warp the entire map. Always verify geometrically!

## Slide 38
BLOCK J
Visual SLAM
SLAM using cameras — the most active research area

## Slide 39
Feature-Based vs. Direct Visual SLAM
39
Feature-Based (Indirect)
Extract ORB/SIFT features
Match across frames, triangulate 3D
Optimize pose graph + 3D points
Examples: ORB-SLAM3, VINS-Mono
Pro: robust, well-understood
Con: discards most image info
Direct (Dense/Semi-Dense)
Use pixel intensities directly
Minimize photometric error
Dense 3D reconstruction possible
Examples: LSD-SLAM, DSO
Pro: uses all image information
Con: sensitive to lighting changes
For mobile robots: feature-based (ORB-SLAM3) is most practical.
Direct shines in AR/VR.

## Slide 40
ORB-SLAM3: Architecture
40
Feature-based visual SLAM (2021). Three parallel threads:
Tracking
(front-end)
ORB extraction, matching,
pose estimation per frame
>
Local Mapping
(mid-end)
Triangulate new points,
local bundle adjustment
>
Loop Closing
(back-end)
DBoW2 place recognition,
pose graph optimization
>
Map Atlas
Multi-map management,
map merging
Supports: mono, stereo, RGB-D + optional IMU.
In ROS 2: ros2-ORB_SLAM3 wrapper or RTAB-Map.

## Slide 41
Visual-Inertial Odometry (VIO)
41
Camera alone (VO):
Fails on pure rotation
Fails textureless surfaces
Monocular: no scale
Slow (30 Hz max)
Camera + IMU (VIO):
IMU fills gaps during fast motion
IMU provides scale + gravity direction
200 Hz IMU + 30 Hz camera
Standard: ARKit, ARCore, drone autopilots
Examples: VINS-Mono, MSCKF, ORB-SLAM3 (IMU mode). The practical choice for visual navigation.

## Slide 42
BLOCK K
SLAM in ROS 2
Practical tools for building maps

## Slide 43
slam_toolbox + Other ROS 2 SLAM Packages
43
Tool | Type | Sensor | Best for
slam_toolbox | Graph 2D | 2D LiDAR | Nav2 standard
Cartographer | Graph 2D/3D | LiDAR+IMU | Large-scale, multi-floor
RTAB-Map | Visual+LiDAR | Camera+LiDAR | Visual SLAM in ROS
ORB-SLAM3 | Feature Visual | Mono/Stereo/RGBD | Research
LIO-SAM | LiDAR-Inertial | 3D LiDAR+IMU | Outdoor, fast motion
MediBot indoor: slam_toolbox.
StreetBot outdoor: Cartographer or LIO-SAM.
Visual: RTAB-Map.

## Slide 44
slam_toolbox: Parameters & Workflow
44
Key parameters:
resolution: 0.05m (cell size)
max_laser_range: max LiDAR range to use
minimum_travel_distance: min move between scans
loop_search_maximum_distance
solver_plugin: Ceres (default)
Workflow:
1. Launch slam_toolbox (online_async)
2. Drive robot around (telop or autonomous)
3. Map builds incrementally in RViz
4. Save: ros2 run nav2_map_server map_saver_cli
5. Use saved map with AMCL + Nav2
Lab: slam_toolbox -> build map -> save -> AMCL (MOD-06) + Nav2 (MOD-09). Full pipeline!

## Slide 45
BLOCK L
SLAM: New Frontiers
Where the field is heading

## Slide 46
Deep Learning SLAM & LiDAR-Inertial SLAM
46
DL-SLAM:
Learned features (SuperPoint, SuperGlue)
More robust than ORB in challenging conditions
End-to-end: image -> pose (DROID-SLAM)
Depth from single image (MonoDepth)
Status: research, needs GPU
LiDAR-Inertial SLAM:
Tightly couple 3D LiDAR + IMU
LIO-SAM, FAST-LIO2
Dense 3D maps at high speed
Works outdoors, tunnels, underground
Most practical 3D SLAM for industry today

## Slide 47
Semantic SLAM & Multi-Robot SLAM
47
Semantic SLAM:
Object-level landmarks (not just points)
'Chair at (3,5)' not 'point at (3,5)'
Enables: 'go to the kitchen' navigation
Kimera, SuMa++, Panoptic SLAM
Combines perception (MOD-07) + SLAM
Multi-Robot SLAM:
Multiple robots map simultaneously
Each builds local sub-map
Meet -> merge sub-maps
Challenges: comms, relative pose, merging
Apps: warehouses, search & rescue

## Slide 48
NeRF & Gaussian Splatting for 3D Reconstruction
48
NeRF (Neural Radiance Fields):
Neural network represents a scene
Input: camera pos -> Output: RGB+density
Photorealistic novel viewpoints
Dense 3D from images only!
Slow training (min to hours)
Gaussian Splatting (2023):
Scene as millions of 3D Gaussians
MUCH faster: real-time rendering!
Quality matches NeRF
SLAM integration: SplaTAM (2024)
Could replace point clouds in future

## Slide 49
Key Takeaways
49
1
SLAM = pose + map
Solve localization and mapping simultaneously.
2
EKF-SLAM: correlations
One Gaussian, O(n^2). Observe one -> improve all.
3
FastSLAM: scalable
Particles + mini-EKFs. O(n log n). Larger maps.
4
Graph-SLAM: modern
Pose graph + optimization. Fixes old errors.
5
Loop closure is key
Recognizing visited places corrects entire map.
6
slam_toolbox in ROS
Graph 2D SLAM. Build map -> Nav2. Standard.

## Slide 50
References
50
1. Thrun, Burgard & Fox (2005). Probabilistic Robotics. Ch. 9-13.
2. Montemerlo et al. (2002). FastSLAM. AAAI.
3. Grisetti et al. (2010). g2o: Graph Optimization. ICRA.
4. Campos et al. (2021). ORB-SLAM3. IEEE Trans. Robotics.
5. Macenski (2021). slam_toolbox. github.com/SteveMacenski
6. Shan & Englot (2020). LIO-SAM. IROS.
7. Mildenhall et al. (2020). NeRF. ECCV.
8. Kerbl et al. (2023). 3D Gaussian Splatting. SIGGRAPH.
9. Hess et al. (2016). Cartographer. ICRA.
Next: MOD-10 — System Integration, Multi-Robot & What's Next

## Slide 51
?