## Slide 1
MOBILE ROBOTS
MOD-04
Sensor Modeling,
Measurement & Fusion
By Dr. Ahmad Abbadi

## Slide 2
The MediBot Challenge
2
MediBot is a hospital delivery robot. Its mission:
Mission
Pharmacy → Ward B (Floor 3) → Lab
Navigate hallways, glass doors, elevator
ZERO collisions — patient safety first
Challenges
Polished floors → wheel slip
Glass doors → invisible to some sensors
People, carts, wheelchairs move unpredictably
Elevator → vibration, tilt, no references
Every sensor lies differently. We model the lies, quantify uncertainty, and combine sensors.
1
Encoders
→
2
Ultrasonic
→
3
LiDAR
→
4
IMU
→
5
Camera
→
6
Radar
→
7
GPS
Indoor (MediBot) → 1-6 | Outdoor (StreetBot) → 7 (GPS)

## Slide 3
BLOCK 1
Wheel Encoders
Count wheel rotations → estimate position

## Slide 4
How Encoders Work
4
Parameter | Value | Meaning
N (ticks/rev) | 500–4096 | Encoder resolution
R (wheel radius) |  | Converts ticks to distance
L (wheelbase) |  | Distance between wheels
Rate | 1–10 kHz | Very fast updates
Wikipedia
N ticks
per rev
Ticks + Movement Direction
A Gray code absolute rotary

## Slide 5
How Encoders Work
4
Δs = distance robot center moved | Δθ = heading change
Δs_R, Δs_L = distance each wheel traveled | L = wheelbase
Update robot position (x,y) and heading (θ) each time step
Intuition:
Count steps → know distance.
Difference between wheels → know turning.
N ticks
per rev

## Slide 6
Feature Extraction: What Encoders Gives Us
5
Sensor → Raw Data → Features → Landmarks for Fusion
Velocity Estimate
Δs / Δt = linear velocity
Δθ / Δt = angular velocity
High rate → smooth velocity signal
Distance Traveled
Cumulative sum of Δs over time
Used for trip odometry
Resets at each localization fix
Motion Detection
Is the robot moving or stopped?
Zero-velocity updates (ZUPT)
Useful for IMU bias correction
As Landmarks: Encoders provide the PREDICTION step in fusion — they tell the system how the robot MOVED. But they drift, so external sensors must CORRECT.

## Slide 7
Encoders: Operate & Failure
6
✅ Use for
Short-term dead reckoning (< 10m)
Velocity estimation for motion model
KF prediction step (fast, continuous)
❌ Fails when
Smooth/wet floors (slip → tick counts lie)
Long distances (drift grows unbounded)
Tight turns (differential errors amplified)
Bumps (wheel bounces = phantom ticks)
💥 FAILURE: MediBot traveled 80m. Odometry says "arrived at elevator." Reality: 3m PAST elevator. Polished floor → micro-slip → heading error accumulated. The uncertainty only grows — nothing corrects it.
→ Need an EXTERNAL sensor to measure the environment. Simplest: ultrasonic (cheap, detects walls and glass).

## Slide 8
BLOCK 2
Ultrasonic Sensors
Ping walls with sound → measure distance

## Slide 9
Ultrasonic: Time-of-Flight
8
TX/RX
WALL
distance = (speed of sound × time) / 2
Speed of sound on air ≈ 343 m/s at 22°C
Divide by 2: sound goes TO wall and BACK
Beam cone: 15–30° wide → returns NEAREST object in cone
c(T) = 331.3 + 0.606 × T
Speed changes with temperature!
Cold room (15°C): 340 m/s
Hot room (37°C): 354 m/s → This is BIAS error if we concede only one speed
★ Key advantage: Ultrasonic DETECTS GLASS! Sound reflects off glass (acoustic impedance mismatch). LiDAR laser (some types) passes through glass. Ultrasonic fills LiDAR's glass blind spot.
Wikipedia

## Slide 10
Feature Extraction: What Ultrasonic Gives Us
9
Sensor → Raw Data → Features → Landmarks for Fusion
Range to Nearest Surface
Single distance value per ping
Good for: wall distance, proximity
Not directional (wide beam cone)
Glass/Transparent Detection
Sound reflects off glass, plastic
Used to flag transparent obstacles
Occupancy Confirmation
"Is there something within 2m?"
Binary: occupied / free
Used for close-range safety zones
As Landmarks: Ultrasonic features are SIMPLE (one range value)

## Slide 11
Ultrasonic: Operate & Failure
10
✅ Use for
Close-range obstacles (< 4m)
Glass door/wall detection
Wall following, elevator proximity
Simple binary safety zone checks
❌ Fails when
Oblique angles > 5° (specular reflection)
Sound-absorbing materials (foam, cotton)
Multiple sensors fire at once (cross-talk)
Range > 4m, open spaces
💥 FAILURE: Hospital lobby (15×20m). Ultrasonic max range = 4m → "no reading." Marble columns at angles → specular reflection. Multiple sensors → cross-talk phantoms.
→ Need: 360° sweep, hundreds of points, fine angular resolution, long range.
→ Next: Block 3 — LiDAR (spinning laser scanner)

## Slide 12
BLOCK 3
LiDAR (2D / 3D)
Spinning laser → hundreds of range-bearing points

## Slide 13
LiDAR: Each Beam Returns (range, angle)
12
Wikipedia
https://encyclopedia.pub/entry/11122

## Slide 14
LiDAR: Each Beam Returns (range, angle)
12
Each beam → (r, φ)
r = distance to surface | φ = angle of beam
360 beams per scan = full circle around robot
To Cartesian:
Convert polar to x,y coordinates
Result: a 2D point cloud of the environment
Spec | 2D LiDAR | 3D LiDAR
Range | 0.1–30 m | 0.1–200 m
Beams/scan | 360–1800 | 16,000–300,000+
Rate | 10–40 Hz | 10–20 Hz
Range noise σ_r | 1–3 cm | 1–5 cm
Angular noise σ_φ | 0.1–0.5° | 0.1–0.3°
2D limitation: scans ONE horizontal plane. Misses table edges above, fallen objects below.

## Slide 15
LiDAR Beam Model: 4 Types of Readings
13
(85%)
NORMAL reading
Laser hits wall → correct
distance + small noise
Bell curve shape
This is what we WANT
(5%)
UNEXPECTED CLOSE
Person's leg, cart wheel
between sensor and wall
Returns shorter range
Exponential shape
(5%)
MISSED (max range)
Glass → laser passes
through! Black surface
→ laser absorbed
Returns z_max
(5%)
RANDOM PHANTOM
Dust, electrical noise
stray reflections
Could be ANY value
Uniform distribution
Most beams are good (85%). But 1 in 7 beams will be wrong in some way — the fusion system must handle this!
Practical alternative — Likelihood Field Model: Precompute a "distance to nearest wall" map. For each LiDAR endpoint, look up how close it is to the nearest expected wall. Close = good match, far = bad match. Much faster than ray-casting. Used by AMCL in ROS.

## Slide 16
Feature Extraction: What LiDAR Gives Us
14
Sensor → Raw Data → Features → Landmarks for Fusion
Line Segments
Walls appear as straight lines
Extract using Hough transform
or split-and-merge algorithm
Corner Points
Where two walls meet = corner
Very stable, repeatable features
Great for localization landmarks
Plane Segments (3D)
Floors, walls, tables as planes
Normal vector + distance
Used in 3D SLAM systems
As Landmarks: LiDAR corners and lines are the PRIMARY landmarks for scan matching and localization. They are stable across visits — same corner = same landmark = position correction.

## Slide 17
LiDAR: Operate & Failure
15
✅ Use for
Hallway mapping & SLAM
Localization
Obstacle avoidance in structured environments
Works in any lighting condition
❌ Fails when
Glass walls/doors (some laser type passes through!)
Mirrors (beam bounces to wrong place)
Black surfaces (absorb laser)
2D: misses above/below scan plane
💥 FAILURE: MediBot enters elevator. Vibrates and tilts. LiDAR scan shifts — but LiDAR has NO knowledge of MediBot’s drift. Doors open Floor 3 → heading off by 3° → after 20m: 1 meter lateral offset.
→ LiDAR sees the WORLD but not ITSELF. Need a sensor that FEELS motion directly.
→ Next: Block 4 — IMU (accelerometer + gyroscope)

## Slide 18
BLOCK 4
IMU (Inertial Measurement Unit)
Feel acceleration and rotation — 200 Hz, no external reference

## Slide 19
IMU: Two Sensors in One Chip
17
Gyroscope (measures rotation)
Output: angular velocity ω (rad/s)
  ω_meas = ω_true + bias + noise
  Bias drifts slowly over time (random walk)
  Integrate ω → get heading angle θ
  Heading error: grows linearly
Accelerometer (measures acceleration)
Output: specific force f (m/s²)
  f_meas = (accel − gravity) + bias + noise
  Must subtract gravity → need orientation!
  1° tilt error → 0.17 m/s² false acceleration
  Position error: grows as QUADRATIC
IMU Error Growth Over Time — Why It Gets Terrible
1s
0.005m
5s
0.12m
15s
0.55m
30s
2.2m
60s
18m
Position error from accelerometer alone

## Slide 20
Feature Extraction: What IMU Gives Us
18
Sensor → Raw Data → Features → Landmarks for Fusion
Gravity Vector
Accelerometer senses gravity direction
→ Tells roll and pitch angles
Only works when not accelerating
Zero-Velocity Detection
When robot stops: accel ≈ gravity only
Used to reset velocity drift
Key trick for correcting IMU bias
Vibration Signature
Different floors = different vibrations
Elevator vs. ramp vs. smooth floor
Can detect surface type changes
As Landmarks: IMU features are INDIRECT — not landmarks on a map, but constraints on MOTION. Zero Update Position and Timing (ZUPT) is especially powerful: when stopped, velocity must be zero → corrects accumulated drift.

## Slide 21
IMU: Operate & Failure
19
✅ Use for
Short-term orientation (< 30 seconds)
Elevator/ramp detection
Bridging gaps between LiDAR scans
ZUPT (zero-velocity updates when stopped)
❌ Fails when
Standalone > 10 seconds (drift explodes)
No external correction available
Strong vibration (saturates accelerometer)
Position from accel: error ∝ T²
💥 FAILURE: 45 seconds without correction → gyro bias drifts 2.25° → 1.5m off.
All corridors look geometrically identical.
MediBot needs to READ the "Ward B" sign and RECOGNIZE a wheelchair vs. a cart.
→ LiDAR = geometry. IMU = motion. Neither = MEANING.
→ Next: Block 5 — Camera (color, texture, text, object recognition)

## Slide 22
BLOCK 5
Camera (RGB + Depth)
See color, texture, text — and measure depth

## Slide 23
Camera: The Pinhole Model
21
(u,v) = pixel position | (X,Y,Z) = 3D point in camera frame
= focal length (pixels) | () = image center
Key Insight:
Projection LOSES depth! A pixel (u,v) could be any point along a ray. Need separate depth sensor (stereo, IR, ToF).
https://stackoverflow.com/questions/68249598/how-to-calculate-the-ray-of-a-camera-with-the-help-of-the-camera-matrix

## Slide 24
Camera: Stereo
21
Stereo Depth Uncertainty — Grows as Z² (quadratic!)
At 1 meter: ±1 cm
Very precise!
Trust this measurement a lot
Good for obstacle avoidance
At 3 meters: ±9 cm
Getting noisy...
OK for sign detection
Unreliable for obstacles
At 5 meters: ±25 cm!
25× worse than 1m!
Unreliable for navigation
Camera is "near-sighted"
Noise depends on distance itself Z
→ HETEROSCEDASTIC:
close = reliable, far = noisy. Fusion must weight close readings MORE.

## Slide 25
Feature Extraction: What Camera Gives Us
22
Sensor → Raw Data → Features → Landmarks for Fusion
Corner Features
Distinctive pixel patterns
Repeatable across viewpoints
Used for visual odometry & SLAM
Edge / Line Features
Door frames, corridor edges
Pair with LiDAR lines for cross-check
Hough transform or LSD detector
Semantic Labels (AI)
"Ward B — Cardiology" (OCR)
Person, wheelchair, cart (detection)
Room type classification
Dense Depth Map
Depth at every pixel (from stereo/IR)
Dense 3D reconstruction (< 4m)
Complements sparse LiDAR points
As Landmarks: Camera features are the RICHEST — from low-level corners (for visual odometry) to high-level semantics (sign reading). They provide MEANING that geometry alone cannot.

## Slide 26
Camera: Operate & Failure
23
✅ Use for
Sign/label reading (OCR)
Person/object detection
Close-range dense 3D (< 4m)
Visual odometry, semantic mapping
❌ Fails when
Sunlight saturates IR depth sensor
Textureless white walls (no stereo match)
Dark corridors (no light = no image)
Glass (IR passes through, like LiDAR)
Limited FoV (~70°) — can't see behind
💥 FAILURE: Supply cart from BEHIND at 2 m/s. Camera faces forward → can't see behind. Sunlight through window → IR depth saturated. Can't measure speed (differentiation amplifies noise).
→ Need: all-weather, wide coverage, DIRECT velocity measurement.
→ Next: Block 6 — Radar (radio waves, Doppler velocity)

## Slide 27
BLOCK 6
Radar (mmWave)
Radio waves → range + angle + VELOCITY for free
https://www.hella.com

## Slide 28
Radar: How FMCW Works + Doppler
25
FMCW Radar:
Transmit chirp → echo delay → range
Chirp = frequency ramp. Echo has time delay.
Beat frequency = range. BW = bandwidth.
Δr = c/(2×BW): 4 GHz → 3.75 cm resolution
Doppler Velocity:
Measures radial velocity DIRECTLY!
No integration (→ no drift like IMU)
No differentiation (→ no noise amplification)
≈ 0.05 m/s — very precise
Method | How | Problem
Encoders → velocity | Differentiate position | Amplifies noise
IMU → velocity | Integrate acceleration | Accumulates bias (drift)
Radar → velocity | Doppler: DIRECT | No drift, no amplification!
Trade-off: angular resolution ~5° (10–50× worse than LiDAR). Two people side-by-side = one blob.
Works through: glass, dust, fog, smoke, rain, any lighting. Does NOT care about visibility.

## Slide 29
Feature Extraction: What Radar Gives Us
26
Sensor → Raw Data → Features → Landmarks for Fusion
Radial Velocity per Target
Each detection has speed attached
Positive = moving away, negative = approaching
Direct, no computation from position
Moving Object Classification
Static vs. dynamic targets via Doppler
Moving person vs. stationary wall
Crucial for dynamic obstacle avoidance
Through-Material Detection
Sees through glass, plastic, drywall
Detects objects behind partitions
Complementary to LiDAR/camera
As Landmarks: Radar features are SPARSE but carry VELOCITY — information no other sensor provides directly. In fusion, radar constrains object MOTION, while LiDAR/camera constrain object POSITION.

## Slide 30
Feature Extraction: What Radar Gives Us
26
https://link.springer.com/article/10.1186/s42467-021-00012-z/figures/1

## Slide 31
Radar: Operate & Failure → Need Absolute Outdoor Reference
27
✅ Use for
Moving object detection + velocity
All-weather sensing (rain, fog, night)
Rear collision avoidance
Seeing through glass/dust/partitions
❌ Fails when
Dense metal environments (multipath clutter)
Very small targets (low radar cross-section)
Need fine-grained shape recognition
Angular resolution too poor for sole navigation
💥 REALIZATION: We have 6 sensors. Indoors, this is enough — LiDAR provides absolute position reference. But what about OUTDOORS? MediBot's sister robot, StreetBot, navigates city sidewalks. No walls to scan. Open sky. Need a GLOBAL position reference.
→ For outdoor: we add a 7th sensor — GPS. Provides absolute position anywhere on Earth.
→ Next: Block 7 — GPS (switching from MediBot to StreetBot)

## Slide 32
BLOCK 7
GPS / GNSS
Absolute position anywhere on Earth — but noisy and slow

## Slide 33
GPS: How It Works (StreetBot Scenario)
29
StreetBot: a last-mile delivery robot navigating city sidewalks, crossings, building lobbies.
Position from satellite timing:
d = c × Δt
4+ satellites → triangulate (x, y, z)
Each satellite broadcasts its position + time.
Receiver measures signal travel time Δt.
With 4+ satellites: solve for position.
Accuracy: 2–5m (open sky), 10–50m (urban canyon)
GPS Error Sources
Atmospheric delay (ionosphere, troposphere)
Multipath: signal bounces off buildings
Urban canyon: buildings block satellites
Slow update rate: only 1–10 Hz
NO signal indoors — completely blind
Parameter | Standard GPS | RTK-GPS
Accuracy | 2–5 m (open sky) | 1–2 cm (with base station)
Update rate | 1–10 Hz | 10–20 Hz
Urban canyon | 10–50 m error | Degraded, needs fallback
Indoors | NO SIGNAL | NO SIGNAL
Cost | $10–$50 | $500–$5,000+

## Slide 34
Feature Extraction: What GPS Gives Us
30
Sensor → Raw Data → Features → Landmarks for Fusion
Absolute Position (lat, lon)
Global reference frame
Does NOT drift over time
But noisy: ±2–5m per reading
Velocity (from Doppler)
GPS Doppler: velocity ±0.1 m/s
More accurate than position!
Useful for heading estimation
Time Synchronization
GPS provides precise UTC time
Used to timestamp all sensors
Critical for multi-sensor fusion
As Landmarks: GPS provides the ABSOLUTE REFERENCE that prevents long-term drift. It's slow and noisy, but it bounds the error. Combined with IMU+encoders (fast, drifting) = the classic complementary fusion pair.

## Slide 35
Measurement Theory
The math behind sensor uncertainty

## Slide 36
The Gaussian (Bell Curve) — Language of Uncertainty
32
μ
← less likely MOST LIKELY less likely →
Two numbers describe everything:
μ (mean) = where the peak is (best guess)
σ (std dev) = how wide the bell is (uncertainty)
68% within μ ± 1σ 95% within μ ± 2σ 99.7% within μ ± 3σ
Small σ → narrow bell → confident sensor
Large σ → wide bell → unreliable sensor

## Slide 37
The Universal Sensor Equation
33
z = h(x) + b + v
Every sensor measurement in robotics follows this form.
z (measurement)
What the sensor REPORTS
The number you actually read
Contains truth + errors
h(x) (truth)
What sensor SHOULD report
If world state is x, the
ideal reading would be h(x)
b (bias)
SYSTEMATIC error
Same direction each time
Fixable by calibration
Example: wrong temperature
v ~ N(0, σ²) (noise)
RANDOM error
Different each time
Cannot remove, only reduce
Described by bell curve
This equation applies to EVERY sensor: encoders, ultrasonic, LiDAR, IMU, camera, radar, GPS. The values of b and σ are different for each.

## Slide 38
The Uncertainty Ellipse — Where the Robot MIGHT Be
34
Start
10m
30m
80m (LOST!)
Each ellipse = region where robot PROBABLY is
Small ellipse = confident. Large ellipse = lost.
With encoders/IMU alone: ellipse ONLY GROWS.
External sensors (LiDAR, GPS) SHRINK the ellipse.
This grow/shrink cycle is the heart of sensor fusion.

## Slide 39
Mahalanobis Distance — Is This Reading Trustworthy?
35
Before accepting any measurement, ask: "How surprising is this reading?"
d_M < 2 → GREEN
Reading matches prediction well
ACCEPT — use in fusion
Sensor is healthy
Most readings should be here
d_M = 2–3 → YELLOW
Reading is a bit surprising
Accept with caution
Maybe increase uncertainty
Monitor if it continues
d_M > 3 → RED
Reading is almost certainly wrong
REJECT — do not use
Sensor may have failed
Flag for health monitoring
d_M = √( innovationᵀ × S⁻¹ × innovation )
innovation = (actual measurement) − (predicted measurement) → the "surprise"
S = combined uncertainty of prediction + measurement
The Mahalanobis distance accounts for HOW UNCERTAIN we are — a 10cm surprise is fine if σ=20cm, but alarming if σ=1cm.

## Slide 40
Heteroscedastic Noise — Not All Measurements Are Equal
36
Some sensors have noise that DEPENDS ON the measurement itself.
Homoscedastic (constant noise)
Noise σ is the same everywhere
Example: ultrasonic σ ≈ 5mm at any range
Simple to handle in fusion
Just set R = σ² = constant
Heteroscedastic (varying noise)
Noise σ depends on distance!
Camera depth: σ_Z ∝ Z²
At 1m: σ=1cm, at 5m: σ=25cm
Must update R for each measurement
Why this matters for fusion:
If you tell the fusion filter that camera depth has constant σ = 5cm, it will OVER-TRUST far readings (which are actually ±25cm) and UNDER-TRUST close readings (which are actually ±1cm). The filter will make bad decisions.
Fix: compute σ_Z = Z²/(f·B) × σ_d for each pixel and set R accordingly.

## Slide 41
Feature Matching
From raw sensor data → landmarks for localization

## Slide 42
What is a Landmark? Types of Landmarks
38
Point Landmarks
LiDAR/camera corners
Distinctive, repeatable
2D or 3D coordinates
Example: wall corner at (3.2, 5.1)
Line/Plane Landmarks
LiDAR wall segments
Parametric: (ρ, α) or (n, d)
Structured environments
Example: corridor wall
Semantic Landmarks
Camera-detected signs, doors
Named: "Ward B entrance"
Rich but harder to extract
Example: room label via OCR
Why landmarks matter:
1. Robot sees landmark A at position p_A in its sensor frame
2. Robot KNOWS landmark A is at position P_A on the map (from a previous visit or a pre-built map)
3. The DIFFERENCE between expected and observed position = position correction
This is exactly the UPDATE step in sensor fusion! Landmarks make uncertainty SHRINK.

## Slide 43
Feature Matching: How to Recognize Landmarks Again
39
Nearest Neighbor Matching
For each feature in current scan:
Find the closest feature in the map
"Closest" in feature descriptor space
Accept if distance < threshold
Fast but sensitive to noise and clutter
RANSAC (Robust Matching)
RANdom SAmple Consensus
1. Pick random feature pairs
2. Compute transformation (rotation+translation)
3. Count how many other features agree
4. Keep the best. Rejects outliers automatically!
Matching Pipeline (for any sensor):
Raw Data
→
Extract Features
→
Describe Features
→
Match to Map
→
Reject Outliers
→
Position Correction
This pipeline runs for LiDAR (scan matching), camera (visual odometry), and even radar (Doppler-based tracking).

## Slide 44
Sensor → Feature → Landmark Summary
40
Sensor | Features | Landmark Type | Matching Method
Encoders | Velocity, distance | — (motion, not landmarks) | Prediction only
Ultrasonic | Range, glass flag | Simple range constraints | Gating / threshold
LiDAR | Corners, lines, planes | Point/line landmarks | ICP, scan matching
IMU | Gravity, ZUPT | — (constraints, not landmarks) | Prediction + ZUPT
Camera | ORB/SIFT, edges, text | Visual landmarks, semantic | NN + RANSAC
Radar | Doppler velocity, RCS | Moving object tracks | Track association
GPS | Lat/lon, velocity | Absolute position fix | Direct measurement
Proprioceptive sensors (encoders, IMU) provide PREDICTION. Exteroceptive sensors (LiDAR, camera, radar, GPS, ultrasonic) provide CORRECTION.

## Slide 45
Sensor Fusion
Combine imperfect sensors → better than any one alone

## Slide 46
Three Types of Fusion
42
Complementary
Sensors give DIFFERENT info
that fills each other's gaps
IMU: fast but drifts
LiDAR: slow but absolute
Together: fast AND accurate
Most common and most powerful
Redundant
Sensors measure the SAME thing
→ increased reliability
LiDAR + Ultrasonic both measure
wall distance. If LiDAR fails on
glass, ultrasonic still works.
Provides fault tolerance
Competitive
Choose the BEST sensor for
current conditions
Bright sunlight: use radar
(camera depth fails)
Dark corridor: use LiDAR+camera
Context-dependent selection
Real systems use all three types simultaneously. The fusion filter handles it automatically via uncertainty weighting.

## Slide 47
The Magic: Fused Result < Any Individual Sensor
43
Sensor A
σ = 5 cm
Sensor B
σ = 10 cm
→
FUSED
σ = 4.5 cm!
Inverse-variance weighting:
weight_A = σ²_B / (σ²_A + σ²_B) = 0.8
weight_B = σ²_A / (σ²_A + σ²_B) = 0.2
More certain sensor → more weight Less certain sensor → less weight
σ_fused = 4.5 cm < σ_A = 5 cm !
Fused is ALWAYS better than the
best individual sensor.

## Slide 48
Predict-Update Cycle (Concept Only — Math in MOD-05)
44
This is how fusion works in practice. The math (Kalman Filter) is in MOD-05.
PREDICT
Source: Encoders + IMU
"Based on how my wheels turned and what my IMU felt, I think I moved 0.5m forward and turned 2° left."
Uncertainty GROWS ↑
(because motion adds noise)
→
UPDATE (CORRECT)
Source: LiDAR / Camera / Radar / GPS
"LiDAR says the wall is at 2.3m. I predicted 2.5m. I was 0.2m off. Correct my position by blending prediction and measurement."
Uncertainty SHRINKS ↓
(measurement corrects drift)
↻ This cycle repeats at the SENSOR RATE (10–200 Hz). Predict-Update-Predict-Update-...
Proprioceptive sensors (encoders, IMU) → FAST predictions that DRIFT
Exteroceptive sensors (LiDAR, camera, radar, GPS) → SLOW corrections that BOUND the drift

## Slide 49
Example: IMU + Odometry + GPS Fusion
45
The classic outdoor fusion combo for StreetBot:
Odometry (1000 Hz)
Fast, continuous
Smooth but DRIFTS
Provides: Δx, Δy, Δθ
Role: PREDICTION
IMU (200 Hz)
Very fast, feels rotation
Orientation + acceleration
Drifts in seconds (bias)
Role: PREDICTION (orientation)
GPS (1–10 Hz)
Slow, noisy (±2–5m)
But ABSOLUTE — no drift!
Position + velocity
Role: CORRECTION
↓ ↓ ↓
EKF FUSION → Fused State Estimate
Smooth (from IMU/odom) + Bounded (from GPS) + Oriented (from IMU)
Best of all three sensors combined. Uncertainty stays small and bounded.
Between GPS updates (100ms gaps): IMU+odom predict. When GPS arrives: corrects drift. Continuous + accurate.

## Slide 50
Fusion Architecture: Centralized vs. Federated
46
Centralized Fusion
All sensors → ONE filter
Single state vector: [x,y,θ,v,bias,...]
✅ Theoretically optimal
❌ Complex, single point of failure
❌ Hard to debug which sensor is wrong
Federated (Decentralized)
Each sensor → own local filter
Local estimates → merged by master
✅ One sensor can fail safely
✅ Easier to test subsystems
❌ Slightly suboptimal (correlations lost)
For safety-critical robots (hospital, delivery): Federated is preferred.
If camera dies → its local filter stops → master continues with remaining sensors.
Multi-rate handling: timestamp everything. When a late measurement arrives, rewind → apply → fast-forward.
Encoders: 1kHz | IMU: 200Hz | Camera: 30Hz | Radar: 15Hz | LiDAR: 10Hz | GPS: 1Hz — all at different rates!

## Slide 51
Sensor Health Monitoring — Graceful Degradation
47
What happens when a sensor FAILS mid-mission?
1. Detect
Mahalanobis distance d_M spikes above threshold (d_M > 3)
2. Degrade
Increase sensor's uncertainty (σ → 10×σ). Filter trusts it less.
3. Disable
If persistent: set weight to zero. Continue with remaining sensors.
4. Recover
When d_M returns to normal: re-enable sensor. Weight restored.
Example: Camera depth fails near sunlit window → d_M spikes → auto-disabled → MediBot continues with LiDAR+ultrasonic+radar → enters shade → camera recovers → auto-re-enabled.

## Slide 52
MediBot + StreetBot: Which Sensor Leads When?
48
Time | Event | Lead Sensor(s)
0–30s | MediBot: corridor travel | LiDAR corrects, Encoders+IMU predict
30s | Glass door approach | ULTRASONIC (glass!) + Camera (sign)
35–50s | Elevator ride (enclosed) | IMU ONLY — drift accumulates
50s | Doors open Floor 3 | LiDAR CORRECTS → uncertainty collapses!
85s | Cart from behind | RADAR (velocity + through glass)
— | StreetBot: open sidewalk | GPS provides absolute correction
— | StreetBot: urban canyon | GPS degrades → LiDAR+IMU take over
— | StreetBot: enters building | GPS = NO SIGNAL → full indoor suite
The fusion system seamlessly hands off between sensors based on availability and reliability. No sensor is "always best."

## Slide 53
DEEP DIVE — Appendix

## Slide 54
DEEP DIVE: Error Propagation via Jacobians
50
If y = f(x) and x ~ N(μ, P), then
J = Jacobian matrix:
This is the FIRST-ORDER approximation — linearize f at the current estimate, then propagate the covariance through the linear approximation.
Odometry:
F = Jacobian w.r.t. state (how current uncertainty propagates)
G = Jacobian w.r.t. control input (how motion noise enters)
Q = control noise covariance: diag(σ²_Δs, σ²_Δθ)
F·P_k·Fᵀ = old uncertainty stretched through motion | G·Q·Gᵀ = new uncertainty added
This is why the covariance ellipse grows and rotates: the Jacobian F stretches it in the direction of motion, and Q adds new uncertainty.

## Slide 55
DEEP DIVE: LiDAR Beam Model Equations
51
Mixture model: each reading is generated by ONE of 4 mechanisms. Mixing weights sum to 1.
for
Gaussian centered on true range. σ_r ≈ 1–3 cm.
for
Exponential: unexpected close object. λ controls steepness.
Point mass at max range. Glass, black surface, open door.
Random: equally likely anywhere. Dust, electrical noise.
Log-likelihood for full scan: ℓ = Σ log p(z_i | x, m) — sum instead of multiply to avoid numerical underflow.

## Slide 56
DEEP DIVE: Stereo Depth Uncertainty Derivation
52
Stereo depth:
f = focal length (pixels), B = baseline (meters), d = disparity (pixels)
Larger disparity → closer object. Zero disparity → infinitely far.
Differentiate:
→
Key: σ_Z grows as Z² — QUADRATIC! This is why camera depth is great at 1m but terrible at 5m.
σ_d ≈ 0.5–2 pixels (sub-pixel stereo matching accuracy).
Noise covariance for fusion:
This R must be RECOMPUTED for each measurement! It's a function of Z, not a constant.
Setting R = constant would over-trust far readings and under-trust close ones.

## Slide 57
DEEP DIVE: Allan Variance for IMU Characterization
53
Record IMU while STATIONARY. Divide into clusters of length τ.
Compute variance of cluster-to-cluster differences. Plot σ(τ) vs τ on log-log.
Slope on log-log | Noise Type | Physical Meaning
−1/2 | White noise (ARW) | Electronic noise, quantization — always present
0 (flat) | Bias instability | Minimum of curve — best the gyro can ever do
+1/2 | Rate random walk | Slow environmental drift — temperature, aging
Read ARW from the −1/2 slope line at τ = 1s. Read bias instability from the minimum of the curve. These parameters go directly into your EKF noise configuration (MOD-05).

## Slide 58
DEEP DIVE: GPS Error Model
54
Position:
b_atm = atmospheric delay (ionosphere + troposphere) — partially correctable
n_multipath = building reflections — worst in urban canyons
n_receiver = internal noise ≈ 0.3–1 m
Error Source | Magnitude | Can Be Corrected?
Ionospheric delay | 2–5 m | Yes (dual-frequency GPS)
Tropospheric delay | 0.2–0.5 m | Partially (models)
Multipath | 1–50 m (urban) | Difficult (antenna design, algorithms)
Satellite geometry (DOP) | 1× – 5× multiplier | Choose better satellite constellation
Receiver noise | 0.3–1 m | No — fundamental limit
RTK-GPS uses a nearby base station to cancel most errors → achieves 1–2 cm accuracy. But requires base station infrastructure and clear sky.

## Slide 59
DEEP DIVE: Polar → Cartesian Uncertainty (LiDAR)
55
Jacobian of the transformation (r,φ) → (x,y). Used to propagate polar noise into Cartesian noise.
Result: at long range, the term dominates → uncertainty ellipse elongates TANGENTIALLY.
At r=4m: angular contribution small. At r=20m: angular contribution 25× larger → accuracy drops at distance.
This is why LiDAR-based SLAM degrades in large open spaces with long-range readings.

## Slide 60
Final Challenge: StreetBot Design Problem
56
Apply everything to a NEW robot in a HARDER environment:
StreetBot Challenges (vs. MediBot)
Rain/snow/fog → camera+LiDAR degrade
Sunlight → camera depth saturated
Uneven terrain → more wheel slip
Moving traffic → need long-range velocity
Glass storefronts everywhere
Your Deliverables
1. Sensor suite: which 7, where, why (20%)
2. Sensor models + noise for each (20%)
3. Feature extraction + landmarks (15%)
4. Fusion architecture + data flow (20%)
5. Top 5 failure scenarios + mitigation (15%)
6. MediBot → StreetBot: what changes? (10%)
Key question: Which sensors change when moving from hospital to sidewalk? What NEW failure modes appear?

## Slide 61
Key Takeaways
57
1
Every sensor lies
Model it: z = h(x) + b + v
2
Quantify uncertainty
Gaussian: μ (best guess), σ (confidence)
3
Errors accumulate
Encoders: linear. IMU: T². Only grows!
4
Extract features
Sensor data → landmarks → map anchors
5
Fuse wisely
Weight ∝ 1/σ² → better than any single sensor
6
Monitor health
Mahalanobis gating → graceful degradation

## Slide 62
References
58
1. Thrun, Burgard & Fox (2005). Probabilistic Robotics. MIT Press. Ch. 5–7.
2. Siegwart, Nourbakhsh & Scaramuzza (2011). Intro to Autonomous Mobile Robots. MIT Press.
3. robot_localization ROS package. github.com/cra-ros-pkg/robot_localization
Next: MOD-05 — Probabilistic Robotics & State Estimation (Kalman Filter derivation)

## Slide 63
?